## Slide 1: Special Topic: Overview and Tricks of the Trade
Eric Prebys

## Slide 2: Multi-stage acceleration
Early synchrotrons had low energy injection and provided all the acceleration in a single stage.
The energy range of a single synchrotron is limited by
  An aperture large enough for the injected beam is unreasonably large at high field.
  Hysteresis effects result in excessive nonlinear terms at low energy (very important for colliders)
Typical range 10-20 for colliders, larger for fixed target
  Fermilab Main Ring: 8-400 GeV (50x)
  Fermilab Tevatron: 150-980 GeV (6.5x)
  LHC: 400-7000 GeV (17x)
The highest energy beams require multiple stages of acceleration, with high reliability at each stage
How is this done?

## Slide 3: Example: CERN Accelerator Complex
50 MeV
1.4 GeV
26 GeV
400 GeV
~7 TeV

## Slide 4: Getting started: Ion sources
CERN proton source
CERN Lead source
Typically 10s of keV and mAs to 10s of mA of current Want to accelerate as fast as possible before space charge blows up the beam!
FNAL H- source. Mix Cesium with Hydrogen to add electron. (why? we’ll get to that)

## Slide 5: Initial acceleration
Old: Static
Static acceleration from Cockcroft-Walton. FNAL = 750 keV
max ~1 MeV
New: RF Quadrupole (RFQ)
RF structure combines an electric focusing quadrupole with a longitudinal accelerating gradient.

## Slide 6: Early stages
The front end of any modern hadron accelerator looks something like this (Fermilab front end)
Low Energy Beam Transport (LEBT, pronounced “lebbit”): 35 keV
Medium Energy Beam Transport (MEBT, pronounced “mebbit”): 750 kEV
Redundant H- sources: 0-35 keV
Solenoidal focusing for low energy beam
200 MHz RFQ: 35750 keV

## Slide 7: Drift Tube (Alvarez) Cavity
Because the velocity is changing quickly, the first linac is generally a Drift Tube Linac (DTL), which can be beta-matched to the accelerating beam.
Put conducting tubes in a larger pillbox, such that inside the tubes E=0
As energy gets higher, switch to “pi-cavities”, which are more efficient
Bunch of pillboxes
Gap spacing changes as velocity increases
Drift tubes contain quadrupoles to keep beam focused
Fermilab low energy linac
Inside


## Slide 8: Linac -> synchrotron injection
Eventually, the linear accelerator must inject into a synchrotron
In order to maximize the intensity in the synchrotron, we can
  Increase the linac current as high as possible and inject over one revolution
    There are limits to linac current
  Inject over multiple (N) revolutions of the synchrotron
    Preferred method
Unfortunately, Liouville’s Theorem says we can’t inject one beam on top of another
  Electrons can be injected off orbit and will “cool” down to the equilibrium orbit via synchrotron radiation.
  Protons can be injected a small, changing angle to “paint” phase space, resulting in increased emittance
Linac emittance
Synchrotron emittance

## Slide 9: Ion (or charge exchange) injection
Instead of ionizing Hydrogen, and electron is added to create H-, which is accelerated in the linac
A pulsed chicane moves the circulating beam out during injection
An injected H- beam is bent in the opposite direction so it lies on top of the circulating beam
The combined beam passes through a foil, which strips the two electrons, leaving a single, more intense proton beam.
Fermilab was converted from proton to H- during the 70’s
CERN still uses proton injection, but is in the process of upgrading (LINAC4 upgrade)
Circulating Beam
Beam at injection
H- beam from LINAC
Stripping foil
Magnetic chicane pulsed to move beam out during injection

## Slide 10: Injection and extraction
We typically would like to extract (or inject) beam by switching a magnetic field on between two bunches (order ~10-100 ns)
Unfortunately, getting the required field in such a short time would result in prohibitively high inductive voltages, so we usually do it in two steps:
fast, weak “kicker”
slower (or DC) extraction magnet with zero field on beam path.

## Slide 11: Extraction hardware
“Lambertson”: usually DC
B
B
circulating beam (B=0)
circulating beam (B=0)
current “blade”
return path
Septum: pulsed, but slower than the kicker
“Slow” extraction elements
“Fast” kicker
usually an impedance matched strip line, with or without ferrites

## Slide 12: Slow Extraction (not important for colliders)
Sometimes fixed target experiments want beam delivered slowly (difficult)
To do this, we generate a harmonic resonance
  Usually sextupoles are used to create a 3rd order resonant instability
Tune the instability so the escaping beam exactly fills the extraction gap between interceptions (3 times around for 3rd order)
  Minimum inefficiency ~(septum thickness)/(gap size)
  Use electrostatic septum made of a plane of wires. Typical parameters
    Septum thickness: .1 mm
    Gap: 10 mm
    Field: 80 kV
particle flow
Particles will flow out of the stable region along lines in phase space into an electrostatic extraction field, which will deflect them into an extraction Lambertson
E

## Slide 13: Standard beam instrumentation
Bunch/beam intensity are measured using inductive toriods
Beam position is typically measured with beam position monitors (BPM’s), which measure the induced signal on a opposing pickups
Longitudinal profiles can be measured by introducing a resistor to measure the induced image current on the beam pipe -> Resistive Wall Monitor (RWM)

## Slide 14: Beam instrumentation (cont’d)
Beam profiles in beam lines can be measured using secondary emission multiwires (MW’s)
Can measure beam profiles in a circulating beam with a “flying wire scanner”, which quickly passes a wire through and measures signal vs time to get profile
Non-destructive measurements include
  Ionization profile monitor (IPM): drift electrons or ions generated by beam passing through residual gas
  Synchrotron light
    Standard in electron machines
    Also works in LHC
Beam profiles in MiniBooNE beam line
Flying wire signal in LHC

## Slide 15: Measuring lattice parameters
The fractional tune is measured by Fourier Transforming signals from the BPM’s
  Sometimes need to excite beam with a kicker
Beta functions can be measured by exciting the beam and looking at distortions
  Can use kicker or resonant (“AC”) dipole
Can also measure the by functions indirectly by varying a quad and measuring the tune shift

## Slide 16: Moving on: The Case for Colliders
If beam hits a stationary proton, the “center of mass” energy is
On the other hand, for colliding beams (of equal mass and energy) it’s
To get the 14 TeV CM design energy of the LHC with a single beam on a fixed target would require that beam to have an energy of 100,000 TeV!
  Would require a ring 10 times the diameter of the Earth!!
Getting to the highest energies requires colliding beams

## Slide 17: Luminosity of Colliding Beams
For equally intense Gaussian beams
Using we have
Geometrical factor: - crossing angle - hourglass effect
Particles in a bunch
Transverse size (RMS)
Collision frequency
Revolution frequency
Number of bunches
Betatron function at collision point  want a small β*!
Normalized emittance
prop. to energy
Particles in bunch
Record e+e- Luminosity (KEK-B): 2.11x1034 cm-2s-1 Record p-pBar Luminosity (Tevatron): 4.06x1032 cm-2s-1 Record Hadronic Luminosity (LHC): 7.0x1033 cm-2s-1 LHC Design Luminosity: 1.00x1034 cm-2s-1

## Slide 18: Limits to β*
 small β* means large β (aperture) at focusing triplet
s
β

## Slide 19: The “squeeze”?
In general, synchrotrons scale all magnetic fields with the momentum, so the optics remain constant – with one exception.
Recall that because of adiabatic damping, beam gets smaller as it accelerates.
This means all apertures must be large enough to accommodate the injected beam.
  This a problem for the large β values in the final focus triplets
For this reason, injection optics have a larger value of β*, and therefor a smaller value of β in the focusing triplets.
After acceleration, beam is “squeezed” to a smaller β* for collision
factor of ~4 for LHC

## Slide 20: First e+e- Collider
ADA (Anello Di Accumulazione) at INFN, Frascati, Italy (1961)
  250 MeV e+ x 250 MeV e-
  L~1025 cm-2s-1
It’s easier to collide e+e-, because synchrotron radiation naturally “cools” the beam to smaller size.

## Slide 21: History: CERN Intersecting Storage Rings (ISR)
First hadron collider (p-p)
Highest CM Energy for 10 years
  Until SppS
Reached it’s design luminosity within the first year.
  Increased it by a factor of 28 over the next 10 years
Its peak luminosity in 1982 was 140x1030 cm-2s-1
  a record that was not broken for 23 years!!

## Slide 22: SppS: First proton-antiproton Collider
Protons from the SPS were used to produce antiprotons, which were collected
These were injected in the opposite direction and accelerated
First collisions in 1981
Discovery of W and Z in 1983
  Nobel Prize for Rubbia and Van der Meer
Energy initially 270+270 GeV
Raised to 315+315 GeV
  Limited by power loss in magnets!
Peak luminosity: 5.5x1030cm-2s-1
  ~.2% of current LHC
design

## Slide 23: Superconductivity: Enabling Technology
The maximum SppS energy was limited by the maximum power loss that the conventional magnets could support in DC operation
  P = I2R proportional to B2
  Maximum practical DC field in conventional magnets ~1T
  LHC made out of such magnets would be roughly the size of Rhode Island!
Highest energy colliders only possible using superconducting magnets
Must take the bad with the good
  Conventional magnets are Superconducting magnets are simple and naturally dissipate complex and represent a great energy as they operate deal of stored energy which must be handled if something goes wrong

## Slide 24: When is a superconductor not a superconductor?
Superconductor can change phase back to normal conductor by crossing the “critical surface”
When this happens, the conductor heats quickly, causing the surrounding conductor to go normal and dumping lots of heat into the liquid Helium“quench
  all of the energy stored in the magnet must be dissipated in some way
Dealing with quenches is the single biggest issue for any superconducting synchrotron!
Tc
Can push the B field (current) too high
Can increase the temp, through heat leaks, deposited energy or mechanical deformation

## Slide 25: Quench Example: MRI Magnet*
*pulled off the web. We recover our Helium.

## Slide 26: Magnet “training”
As new superconducting magnets are ramped, electromechanical forces on the conductors can cause small motions.
The resulting frictional heating can result in a quench
Generally, this “seats” the conductor better, and subsequent quenches occur at a higher current.
This process is knows as “training”

## Slide 27: Milestones on the Road to a Superconducting Collider
1911 – superconductivity discovered by Heike Kamerlingh Onnes
1957 – superconductivity explained by Bardeen, Cooper, and Schrieffer
  1972 Nobel Prize (the second for Bardeen!)
1962 – First commercially available superconducting wire
  NbTi, the “industry standard” since
1978 – Construction began on ISABELLE, first superconducting collider (200 GeV+200 GeV) at Brookhaven.
  1983, project cancelled due to design problems, budget overruns, and competition from…

## Slide 28: Tevatron: First Superconducting Synchrotron
1968 – Fermilab Construction Begins
1972 – Beam in Main Ring
  (normal magnets)
Plans soon began for a superconducting collider to share the ring.
  Dubbed “Saver Doubler” (later “Tevatron”)
1985 – First proton-antiproton collisions in Tevatron
  Most powerful accelerator in the world for the next quarter century
1995 – Top quark discovery
Reached L=4.06x1032 cm-2s-1
  Breaking ISR p-p record
2011 – Tevatron shut down after successful LHC startup
Main Ring
Tevatron

## Slide 29: The Fermilab Accelerator Complex
MiniBooNE/BNB
NUMI

## Slide 30: “Stack and Store” cycle
The Linac accelerated beam to 400 MeV, and injected it into the Booster
The Booster accelerated beam from 400 MeV to 8 GeV and transferred it to the Main Injector.
The Main Injector accelerated beam from 8 GeV to 120 GeV, and this beam was used to produce 8 GeV antiprotons.
Antiprotons were accumulated for roughly 1 day.
These were then accelerated by the Main Injector to 150 GeV, and injected into the Tevatron.
The Tevatron accelerated protons and antiprotons to 980 GeV and collided them for ~1 day.

## Slide 31: Fermilab Antiproton Source
120 GeV protons strike a target, producing many things, including antiprotons.
a Lithium lens focuses these particles (a bit)
a bend magnet selects the negative particles around 8 GeV. Everything but antiprotons decays away.
The antiproton ring consists of 2 parts
– the Debuncher – the Accumulator.

## Slide 32: Antiproton Source – debunching
Particles enter with a narrow time spread and broad energy spread.
High (low) energy pbars take more (less) to go around…
…and the RF is phased so they are decelerated (accelerated),
resulting in a narrow energy spread and broad time spread.
At this point, the pBars are transferred to the accumulator, where they are “stacked”

## Slide 33: Stochastic cooling of antiprotons
Positrons will naturally “cool” (approach a small equilibrium emittance) via synchrotron radiation.
Antiprotons must rely on active cooling to be useful in colliders.
Principle: consider a single particle which is off orbit. We can detect its deviation at one point, and correct it at another:
But wait! If we apply this technique to an ensemble of particles, won’t it just act on the centroid of the distribution? Yes, but…
Stochastic cooling relies on “mixing”, the fact that particles of different momenta will slip in time and the sampled combinations will change.
Statistically, the mean displacement will be dominated by the high amplitude particles and over time the distribution will cool.

## Slide 34: History of Fermilab Luminosity
87 Run
Run 0
Run 1a
Run 1b
Run II
ISR (pp) record
SppS record
Discovery of top quark (1995)
Main Injector Construction
Original Run II Goal

## Slide 35: Proton-Proton vs. Proton-antiproton
Beyond a few hundred GeV, most interactions take place between gluons and/or virtual “sea” quarks.
  No real difference between proton-antiproton and proton-proton
Because of the symmetry properties of the magnetic field, a particle going in one direction will behave exactly the same as an antiparticle going in the other direction
  Can put protons and antiprotons in the same ring
    This is how the SppS (CERN) and the Tevatron (Fermilab) did it.
The problem is that antiprotons are hard to make
  Can get >1 positron for every electron on a production target
  Can only get about 1 antiproton for every 50,000 protons on target!
  It took a day to make enough antiprotons for a “store” in the Fermilab Tevatron
  Ultimately, the luminosity is limited by the antiproton current.

## Slide 36: Antiprotons for LHC?
At the design luminosity of the LHC, the antiproton “burn” rate would be
The is about 15 times the maximum production rate achieved by the Fermilab antiproton source
  No one has a good idea how to do this
  The required proton beam would be megawatts (=neutrino beam)
For this reason, it was long recognized that the next collider would be proton proton.

## Slide 37: A Detour on the Road to Higher Energy
1980’s - US begins planning in earnest for a 20 TeV+20 TeV “Superconducting Super Collider” or (SSC).
  87 km in circumference!
  Two separate beams (like the ISR)
  Considered superior to the “Large Hadron Collider” (LHC) then being proposed by CERN.
1987 – site chosen near Dallas, TX
1989 – construction begins
1993 – amidst cost overruns and the end of the Cold War, the SSC is cancelled after 17 shafts and 22.5 km of tunnel had been dug.
2001 – After the end of the LEP program at CERN, work begins on reusing the 27 km tunnel for the 7 TeV+ 7 TeV LHC

## Slide 38: LHC: Location, Location, Location…
Tunnel originally dug for LEP
  Built in 1980’s as an electron positron collider
  Max 100 GeV/beam, but 27 km in circumference!!
/LHC
My House (1990-1992)

## Slide 39: LHC Layout and Numbers
Design:
7 TeV+7 TeV proton beams
  Can’t make enough antiprotons for the LHC
  Magnets have two beam pipes, one going in each direction.
Stored beam energy 150 times more than Tevatron
  Each beam has only 5x10-10 grams of protons, but has the energy of a train going 100 mph!!
These beams are focused to a size smaller than a human hair to collide with each other!
27 km in circumference
2 major collision regions: CMS and ATLAS
2 “smaller” regions: ALICE and LHCb

## Slide 40: Standard LHC FODO Cell
e+e- or proton-antiproton (opposite charge) colliders had particles going in opposite directions in the same beam pipe
Because the LHC collides protons (same charge), the magnets have two apertures with opposite fields
dipoles (Bmax = 8.3 T)
quadrupoles

## Slide 41: Nominal LHC Parameters Compared to Tevatron
Parameter | Tevatron | “nominal” LHC
Circumference | 6.28 km (2*PI) | 27 km
Beam Energy | 980 GeV | 7 TeV
Number of bunches | 36 | 2808
Protons/bunch | 275x109 | 115x109
pBar/bunch | 80x109 | -
Stored beam energy | 1.6 + .5 MJ | 366+366 MJ*
Magnet stored energy | 400 MJ | 10 GJ
Peak luminosity | 3.3x1032 cm-2s-1 | 1.0x1034 cm-2s-1
Main Dipoles | 780 | 1232
Bend Field | 4.2 T | 8.3 T
Main Quadrupoles | ~200 | ~600
Operating temperature | 4.2 K (liquid He) | 1.9K (superfluid He)
*Each beam = TVG@150 km/hr  very scary numbers
1.0x1034 cm-2s-1 ~ 50 fb-1/yr= ~5 x total TeV data
Increase in cross section of up to 5 orders of magnitude for some physics processes

## Slide 42: Experimental reach of LHC vs. Tevatron
W (MW=80 GeV)
Z (MZ=91 GeV)
The rate of physical processes depends strongly on energy
  For some of the most interesting searches, the rate at the LHC will be 10-100 times the rate at the Tevatron.
Nevertheless, still need about 30 times the luminosity of the Tevatron to study the most important physics

## Slide 43: Protecting the Machine: Multi-stage Collimation

## Slide 44: September 10, 2008: The Big Day
Plotted the biggest media event in the history of science
This plot shows how far beam had been prior to Sept. 10.
Progress prior to event

## Slide 45: Orbit correction
Generally, beam lines or synchrotrons will have beam position monitors (BPM’s) and correction dipoles (trims)
We would like to use the trims to cancel out the effect of beamline imperfectins, ie
Can express this as a matrix and invert to solve with standard techniques
  If n=m, can just invert
  If n>m, can minimize RMS
Cancel displacement at BPM i due to imperfections
Setting of trim j

## Slide 46: Example: Injection test
Aperture scan: move beam around until you hit something
Mis-steering
Beam direction
Injection region aperture point 2

## Slide 47: Close call: the event that almost wasn’t
From the LHC eLogBook:
Cryogenic problems meant parts of the ring were not cold until a couple of hours before the start (with the world media watching)!

## Slide 48: Nevertheless, the party started on schedule
Fermilab “Pajama Party”
CERN Control Centre (CCC)

## Slide 49: Started with beam one (clockwise) at 9:35
General procedure
  Proceed one octant at a time, closing collimators at the next point.
  Take several shots to correct beam deviation
Beam 1 direction
Beam 2 direction (separate display)
New territory!

## Slide 50: Beam seen in CMS

## Slide 51: Timeline (CEDT)
9:35 – First beam injected
9:58 – beam past CMS to point 6 dump
10:15 – beam to point 1 (ATLAS)
10:26 – First turn!
…and there was much rejoicing

## Slide 52: After initial circulation: captured beam
Everything was going great until something very bad happened on September 19th
  Initially, CERN kept a tight lid on news
Turn Number
Time

## Slide 53: Nature abhors a (news) vacuum…
Italian newspapers were very poetic (at least as translated by “Babel Fish”):
"the black cloud of the bitterness still has not been dissolved on the small forest in which they are dipped the candid buildings of the CERN"
“Lyn Evans, head of the plan, support that it was better to wait for before igniting the machine and making the verifications of the parts.“*
Or you could Google “What really happened at CERN”:
* “Big Bang, il test bloccato fino all primavera 2009”, Corriere dela Sera, Sept. 24, 2008
**
**http://www.rense.com/general83/IncidentatCERN.pdf

## Slide 54: What (really) really happened on September 19th*
Sector 3-4 was being ramped to 9.3 kA, the equivalent of 5.5 TeV
  All other sectors had already been ramped to this level
  Sector 3-4 had previously only been ramped to 7 kA (4.1 TeV)
At 11:18AM, a quench developed in the splice between dipole C24 and quadrupole Q24
  Not initially detected by quench protection circuit
  Power supply tripped at .46 sec
  Discharge switches activated at .86 sec
Within the first second, an arc formed at the site of the quench
  The heat of the arc caused Helium to boil.
  The pressure rose beyond .13 MPa and ruptured into the insulation vacuum.
  Vacuum also degraded in the beam pipe
The pressure at the vacuum barrier reached ~10 bar (design value 1.5 bar). The force was transferred to the magnet stands, which broke.
*Official talk by Philippe LeBrun, Chamonix, Jan. 2009

## Slide 55: Pressure forces on SSS vacuum barrier
Vacuum
1/3 load on cold mass (and support post)
~23 kN
1/3 load on barrier
~46 kN
Pressure
10 bar
Total load on 1 jack ~70 kN
V. Parma

## Slide 56: Collateral damage: magnet displacements
QQBI.27R3

## Slide 57: Collateral damage: secondary arcs
QQBI.27R3 M3 line
QBBI.B31R3 M3 line

## Slide 58: Collateral damage: ground supports

## Slide 59: Collateral damage: Beam Vacuum
LSS3
LSS4
OK
Debris
MLI
Soot
The beam pipes were polluted with thousands of pieces of MLI and soot, from one extremity to the other of the sector
clean
MLI
soot
Arc burned through beam vacuum pipe

## Slide 60: Important questions about Sept. 19
Why did the joint fail?
  Inherent problems with joint design
    No clamps
    Details of joint design
    Solder used
  Quality control problems
Why wasn’t it detected in time?
  There was indirect (calorimetric) evidence of an ohmic heat loss, but these data were not routinely monitored
  The bus quench protection circuit had a threshold of 1V, a factor of >1000 too high to detect the quench in time.
Why did it do so much damage?
  The pressure relief system was designed around an MCI Helium release of 2 kg/s, a factor of ten below what occurred.

## Slide 61: What happened?
Working theory: A resistive joint of about 220 nΩ with bad electrical and thermal contacts with the stabilizer
No electrical contact between wedge and U-profile with the bus on at least 1 side of the joint
No bonding at joint with the U-profile and the wedge
A. Verweij
Loss of clamping pressure on the joint, and between joint and stabilizer
Degradation of transverse contact between superconducting cable and stabilizer
Interruption of longitudinal electrical continuity in stabilizer
Problem: this is where the evidence used to be

## Slide 62: Interim Improvements (2008-2009)
Bad joints
  Test for high resistance and look for signatures of heat loss in joints
  Warm up to repair any with signs of problems (additional three sectors)
Quench protection
  Old system sensitive to 1V
  New system sensitive to .3 mV
Pressure relief
  Warm sectors (4 out of 8)
    Install 200mm relief flanges
    Enough capacity to handle even the maximum credible incident (MCI)
  Cold sectors
    Reconfigure service flanges as relief flanges
    Reinforce floor mounts
    Enough capacity to handle the incident that occurred, but not quite the MCI

## Slide 63: After the first shutdown
2009
  November 20th: Particles circulate again
  Based on a detailed thermal model of the joints and failure scenarios, it’s decided to limit energy to 3.5 TeV
2010
  March 30th: 3.5 + 3.5 TeV collisions
    Energy limited by flaw which caused accident
2012
  January (Chamonix meeting): based on observed performance and revised modeling, it’s decided to increase energy to 4 TeV.
  April 5th: Energy increased to 4 + 4 TeV
  July 4th: Announced the discovery of the Higgs
2013
  Feb. 14th: Start 2 year shutdown to address design flaw and allow full energy operation
  ALL (~10000) joints resoldered, clamped and radiographed.
  Remaining sectors outfitted with improved pressure relief.

## Slide 64: After the shutdown
After repairs are completed, accelerator will come back up in 2015 at something close to the design energy
  At least 6.5 TeV/beam
The LHC will be the centerpiece of the world’s energy frontier physics program for at least the next 15-20 years.

## Slide 65: Longer Term: The Big Picture
3000 fb-1
~ 50 years at nominal LHC luminosity!
The future begins now
How can we increase the luminosity??

## Slide 66: Limits to LHC Luminosity*
Total beam current, limited by machine protection(!), e-cloud and other instabilities
β*, limited by
magnet technology
chromatic effects
Brightness, limited by
PSB injection energy
PS
Max tune-shift
Geometric factor, related to crossing angle…
*see, eg, F. Zimmermann, “CERN Upgrade Plans”, EPS-HEP 09, Krakow, for a thorough discussion of luminosity factors.

## Slide 67: Current LHC Acceleration Sequence and Brightness Issues
Schematic ONLY. Scale and orientation not correct
Space Charge Limitations at Booster and PS injection
Transition crossing in PS and SPS

## Slide 68: Addressing brightness issues
There are plans to address two of the major sources of emittance blowup in the injector chain
  Injection from the LINAC into the PS Booster
    The current linac uses proton painting at 50 MeV
    New LINAC4 will use ion injection at 160 MeV
  Space charge at injection into PS
    Extraction energy of the PS Booster will be increased from 1.4 to 2.0 GeV
These upgrades are scheduled to take place during Long Shutdown 2

## Slide 69: Limits to β*
 small β* means large β (aperture) at focusing triplet
s
β
β distortion of off-momentum particles (affects collimation)

## Slide 70: The Case for New Quadupoles
HL-LHC Proposal: β*=55 cm  β*=10 cm
Just like classical optics
  Small, intense focus big, powerful lens
  Small β*huge β at focusing quad
  Need bigger quads to go to smaller β*
Existing quads
70 mm aperture
200 T/m gradient
Proposed for upgrade
140 mm aperture
200 T/m gradient
Field 70% higher at pole face
 Beyond the limit of NbTi

## Slide 71: Motivation for Nb3Sn
Nb3Sn can be used to increase aperture/gradient and/or increase heat load margin, relative to NbTi
120 mm aperture
Limit of NbTi magnets
Very attractive, but no one has ever built accelerator quality magnets out of Nb3Sn
Whereas NbTi remains pliable in its superconducting state, Nb3Sn must be reacted at high temperature, causing it to become brittle
  Must wind coil on a mandril
  React
  Carefully transfer to yolk

## Slide 72: US-LARP Magnet Development Tree
LHC Prototype 4 m long
150 mm bore
Being designed jointly with CERN

## Slide 73: IR Layout: the need for a crossing angle
Nominal Bunch spacing: 7.5 m
Collision spacing: 3.75 m
~2x15 parasitic collisions per IR
  Remember: ALL of these would cause equal tune shifts
IP
Final Triplet
Separation Dipole
~59 m
Need Crossing Angle

## Slide 74: Crossing Angle Considerations
Crossing angle reduces luminosity
“Piwinski Angle”
Minor effect at current β*, but largely cancels benefit of lowering β*

## Slide 75: Baseline Approach: Crab Cavities
Technical Challenges
  Crab cavities have only barely been shown to work.
    Never in hadron machines
  LHC bunch length  low frequency (400 MHz)
  19.2 cm beam separation  “compact” (exotic) design
Additional benefit
  Crab cavities may help level luminosity!

## Slide 76: Luminosity Leveling
Original goal of luminosity upgrade: >1035 cm-2s-1
  Leads to unacceptable pileup in detectors
New goal: 5x1034 leveled luminosity
Options
  Crab cavities
  β* modifications
  Lateral separation
“Crab kissing” – sort of complicated

## Slide 77: Long Term Plan*
*L. Rossi, LARP/HL-LHC Meeting, Nov. 2013

## Slide 78: Summary: Evolution of the Energy Frontier
~a factor of 10 every 15 years
This will not continue

## Slide 79: What next?
The energy of Hadron colliders is limited by feasible size and magnet technology. Options:
  Get very large (~100 km circumference)
  More powerful magnets (requires new technology)
All accelerator magnets based on this
Future magnets could be based on this

## Slide 80: Future Circular Collider (FCC)
Currently being discussed for ~2030s
80-100 km in circumference
Niobium-3-Tin (Nb3Sn) magnets.
~100 TeV center of mass energy

## Slide 81: Some things to think about for FCC
Recall that luminosity is given by
If we wanted to keep just 1034 luminosity (probably not enough), the γ factor would let us back down on Nb a bit, but to keep the crossing rate the number of bunches would increase with the circumference so stored energy would be
What are the options to make it more compact, and or go to even higher energies?
~1 ton on TNT = Scary!

## Slide 82: Superconductor Options
Traditional
  NbTi
    Basis of ALL superconducting accelerator magnets to date
    Largest practical field ~8T
  Nb3Sn
    Advanced R&D
    Being developed for large aperture/high gradient quadrupoles
    Larges practical field ~14T
High Temperature
  Industry is interested in operating HTS at moderate fields at LN2 temperatures. We’re interested in operating them at high fields at LHe temperatures.
    MnB2
      promising for power transmission
      can’t support magnetic field.
    YBCO
      very high field at LHe
      no cable (only tape)
    BSCCO (2212)
      strands demonstrated
      unmeasureably high field at LHe
Focusing on this, but very expensive
 pursue hybrid design

## Slide 83: Potential Designs
P. McIntyre 2005 – 24T ss Tripler, a lot of Bi-2212 , Je = 800 A/mm2
E. Todesco 2010
20 T, 80% ss
30% NbTi
55 %NbSn
15 %HTS
All Je < 400 A/mm2

## Slide 84: Some other important accelerators (past):
LEP (at CERN):
  27 km in circumference - e+e- - Primarily at 2E=MZ (90 GeV) - Pushed to ECM=200GeV - L = 2E31 - Highest energy circular e+e- collider that will ever be built. - Tunnel now houses LHC
SLC (at SLAC):
  2 km long LINAC accelerated electrons AND positrons on opposite phases. - 2E=MZ (90 GeV) - polarized - L = 3E30 - Proof of principle for linear collider

## Slide 85: B-Factories
- B-Factories collide e+e- at ECM = M((4S)). -Asymmetric beam energy (moving center of mass) allows for time-dependent measurement of B-decays to study CP violation.
KEKB (Belle Experiment):
- Located at KEK (Japan) - 8GeV e- x 3.5 GeV e+ - Peak luminosity 1E34
PEP-II (BaBar Experiment)
- Located at SLAC (USA) - 9GeV e- x 3.1 GeV e+ - Peak luminosity 0.6E34

## Slide 86: Relativistic Heavy Ion Collider (RHIC)
- Located at Brookhaven:
Can collide protons (at 28.1 GeV) and many types of ions up to Gold (at 11 GeV/amu).
Luminosity: 2E26 for Gold
Goal: heavy ion physics, quark-gluon plasma, ??

## Slide 87: Continuous Electron Beam Accelerator Facility (CEBAF)
Locate at Jefferson Laboratory, Newport News, VA
6GeV e- at 200 uA continuous current
Nuclear physics, precision spectroscopy, etc

## Slide 88: Research machines: just the tip of the iceberg

## Slide 89: Example: Spallation Neutron Source (Oak Ridge, TN)
A 1 GeV Linac will load 1.5E14 protons into a non-accelerating synchrotron ring.
These are fast extracted onto a Mercury target
This happens at 60 Hz -> 1.4 MW
Neutrons are used for biophysics, materials science, industry, etc…

## Slide 90: Light sources: too many to count
Put circulating electron beam through an “undulator” to create synchrotron radiation (typically X-ray)
Many applications in biophysics, materials science, industry.
New proposed machines will use very short bunches to create coherent light.

## Slide 91: Other uses of accelerators
Radioisotope production
Medical treatment
Electron welding
Food sterilization
Catalyzed polymerization
Even art…
In a “Lichtenberg figure”, a low energy electron linac is used to implant a layer of charge in a sheet of lucite. This charge can remain for weeks until it is discharged by a mechanical disruption.

## Slide 92: The future: International Linear Collider (ILC)?
LEP was the limit of circular e+e- colliders
  Next step must be linear collider
  Proposed ILC 30 km long, 250 x 250 GeV e+e-
BUT, we don’t yet know whether that’s high enough energy to be interesting
  Need to wait for LHC results
  What if we need more?

## Slide 93: “Compact” (ha ha) Linear Collider (CLIC)?
Use low energy, high current electron beams to drive high energy accelerating structures
Up to 1.5 x 1.5 TeV, but VERY, VERY hard

## Slide 94: Muon colliders?
Muons are pointlike, like electrons, but because they’re heavier, synchrotron radiation is much less of a problem.
Unfortunately, muons are unstable, so you have to produce them, cool them, and collide them, before they decay.

## Slide 95: Wakefield accelerators?
Many advances have been made in exploiting the huge fields that are produced in plasma oscillations.
Potential for accelerating gradients many orders of magnitude beyond RF cavities.
Still a long way to go for a practical accelerator.