## Slide 1: Tricks of the trade
Eric Prebys, UC Davis

## Slide 2: Multi-stage Acceleration
Early synchrotrons had low energy injection and provided all the acceleration in a single stage.
The energy range of a single synchrotron is limited by
  An aperture large enough for the injected beam is unreasonably large at high field.
  Hysteresis effects result in excessive nonlinear terms at low energy (very important for colliders)
Typical range 10-20 for colliders, larger for fixed target
  Fermilab Main Ring: 8-400 GeV (50x)
  Fermilab Tevatron: 150-980 GeV (6.5x)
  LHC: 400-7000 GeV (17x)
The highest energy beams require multiple stages of acceleration, with high reliability at each stage
How is this done?

## Slide 3: Example: CERN Accelerator Complex
50 MeV
1.4 GeV
26 GeV
400 GeV
~7 TeV

## Slide 4: Getting Started: Ion Sources
CERN proton source
CERN Lead source
Typically 10s of keV and mAs to 10s of mA of current. Want to accelerate as fast as possible before space charge blows up the beam!
FNAL H- source. Mix Cesium with Hydrogen to add electron. (why? we’ll get to that)

## Slide 5: Initial Acceleration
Old: Static
Static acceleration from Cockcroft-Walton. FNAL = 750 keV
max ~1 MeV
New: RF Quadrupole (RFQ)
RF structure combines an electric focusing quadrupole with a longitudinal accelerating gradient.

## Slide 6: Early Stages
The front end of any modern hadron accelerator looks something like this (Fermilab front end)
Low Energy Beam Transport (LEBT, pronounced “lebbit”): 35 keV
Medium Energy Beam Transport (MEBT, pronounced “mebbit”): 750 kEV
Redundant H- sources: 0-35 keV
Solenoidal focusing for low energy beam
200 MHz RFQ: 35750 keV

## Slide 7: Drift Tube (Alvarez) Cavity
Because the velocity is changing quickly, the first linac is generally a Drift Tube Linac (DTL), which can be beta-matched to the accelerating beam.
Put conducting tubes in a larger pillbox, such that inside the tubes E=0
As energy gets higher, switch to “pi-cavities”, which are more efficient
Bunch of pillboxes
Gap spacing changes as velocity increases
Drift tubes contain quadrupoles to keep beam focused
Fermilab low energy linac
Inside


## Slide 8: Linac -> Synchrotron Injection
Eventually, the linear accelerator must inject into a synchrotron
In order to maximize the intensity in the synchrotron, we can
  Increase the linac current as high as possible and inject over one revolution
    There are limits to linac current
  Inject over multiple (N) revolutions of the synchrotron
    Preferred method
Unfortunately, Liouville’s Theorem says we can’t inject one beam on top of another
  Electrons can be injected off orbit and will “cool” down to the equilibrium orbit via synchrotron radiation.
  Protons can be injected a small, changing angle to “paint” phase space, resulting in increased emittance
Linac emittance
Synchrotron emittance

## Slide 9: Ion (or Charge Exchange) Injection
Instead of ionizing Hydrogen, and electron is added to create H-, which is accelerated in the linac
A pulsed chicane moves the circulating beam out during injection
An injected H- beam is bent in the opposite direction so it lies on top of the circulating beam
The combined beam passes through a foil, which strips the two electrons, leaving a single, more intense proton beam.
Fermilab was converted from proton to H- during the 70’s
CERN still uses proton injection, but is in the process of upgrading (LINAC4 upgrade)
Circulating Beam
Beam at injection
H- beam from LINAC
Stripping foil
Magnetic chicane pulsed to move beam out during injection

## Slide 10: Injection and Extraction
We typically would like to extract (or inject) beam by switching a magnetic field on between two bunches (order ~10-100 ns)
Unfortunately, getting the required field in such a short time would result in prohibitively high inductive voltages, so we usually do it in two steps:
fast, weak “kicker”
slower (or DC) extraction magnet with zero field on beam path.

## Slide 11: Extraction Hardware
“Lambertson”: usually DC
B
B
circulating beam (B=0)
circulating beam (B=0)
current “blade”
return path
Septum: pulsed, but slower than the kicker
“Slow” extraction elements
“Fast” kicker
usually an impedance matched strip line, with or without ferrites

## Slide 12: Slow Extraction (not important for colliders)
Sometimes fixed target experiments want beam delivered slowly (difficult)
To do this, we generate a harmonic resonance
  Usually sextupoles are used to create a 3rd order resonant instability
Tune the instability so the escaping beam exactly fills the extraction gap between interceptions (3 times around for 3rd order)
  Minimum inefficiency ~(septum thickness)/(gap size)
  Use electrostatic septum made of a plane of wires. Typical parameters
    Septum thickness: .1 mm
    Gap: 10 mm
    Field: 80 kV
particle flow
Particles will flow out of the stable region along lines in phase space into an electrostatic extraction field, which will deflect them into an extraction Lambertson
E

## Slide 13: Standard Beam Instrumentation
Bunch/beam intensity are measured using inductive toriods
Beam position is typically measured with beam position monitors (BPM’s), which measure the induced signal on a opposing pickups
Longitudinal profiles can be measured by introducing a resistor to measure the induced image current on the beam pipe -> Resistive Wall Monitor (RWM)

## Slide 14: Beam Instrumentation (cont’d)
Beam profiles in beam lines can be measured using secondary emission multiwires (MW’s)
Can measure beam profiles in a circulating beam with a “flying wire scanner”, which quickly passes a wire through and measures signal vs time to get profile
Non-destructive measurements include
  Ionization profile monitor (IPM): drift electrons or ions generated by beam passing through residual gas
  Synchrotron light
    Standard in electron machines
    Also works in LHC
Beam profiles in MiniBooNE beam line
Flying wire signal in LHC

## Slide 15: Measuring Lattice Parameters
The fractional tune is measured by Fourier Transforming signals from the BPM’s
  Sometimes need to excite beam with a kicker
Beta functions can be measured by exciting the beam and looking at distortions
  Can use kicker or resonant (“AC”) dipole
Can also measure the by functions indirectly by varying a quad and measuring the tune shift

## Slide 16: Understanding Cross Sections
The formalism of cross sections was derived for Rutherford scattering, in which a scattered solid angle was mapped to an incident cross sectional area
It can be generalized to represent the probability of any sort of particle interaction

## Slide 17: Thin target approximation
If the total probability that a particle will interact is small, then the probability of a particular interaction for one incident particle, will be given by
Target thickness [L]
Target number density [L-3]

## Slide 18: Luminosity
The relationship of the beam to the rate of observed physics processes is given by the “Luminosity”
Rate
Cross-section (“physics”)
“Luminosity”
Standard unit for Luminosity is cm-2s-1 Standard unit of cross section is “barn”=10-24 cm2 Integrated luminosity is usually in barn-1,where
nb-1 = 109 b-1, fb-1=1015 b-1, etc
Incident rate
Target number density
Target thickness
Example: MiniBooNe primary target:
For (thin) fixed target:

## Slide 19: Colliding Beam Luminosity
Circulating beams typically “bunched”
(number of interactions)
Cross-sectional area of beam
Total Luminosity:
Circumference of machine
Number of bunches
crossing rate

## Slide 20: Luminosity of Colliding Beams
For equally intense Gaussian beams
Using we have
Geometrical factor: - crossing angle - hourglass effect
Particles in a bunch
Transverse size (RMS)
Collision frequency
Revolution frequency
Number of bunches
Betatron function at collision point  want a small β*!
Normalized emittance
prop. to energy
Particles in bunch
Record e+e- Luminosity (KEK-B): 2.11x1034 cm-2s-1 Record p-pBar Luminosity (Tevatron): 4.06x1032 cm-2s-1 Record Hadronic Luminosity (LHC): 2.06x1034 cm-2s-1

## Slide 21: Limits to β*
 small β* means large β (aperture) at focusing triplet
s
β

## Slide 22: The “Squeeze”?
In general, synchrotrons scale all magnetic fields with the momentum, so the optics remain constant – with one exception.
Recall that because of adiabatic damping, beam gets smaller as it accelerates.
This means all apertures must be large enough to accommodate the injected beam.
  This a problem for the large β values in the final focus triplets
For this reason, injection optics have a larger value of β*, and therefor a smaller value of β in the focusing triplets.
After acceleration, beam is “squeezed” to a smaller β* for collision
factor of ~4 for LHC

## Slide 23: Orbit correction
Generally, beam lines or synchrotrons will have beam position monitors (BPM’s) and correction dipoles (trims)
We would like to use the trims to cancel out the effect of beamline imperfectins, ie
Can express this as a matrix and invert to solve with standard techniques
  If n=m, can just invert
  If n>m, can minimize RMS
Cancel displacement at BPM i due to imperfections
Setting of trim j

## Slide 24: Example: First Beam through LHC (Sept. 10, 2008)
General procedure
  Proceed one octant at a time, closing collimators at the next point.
  Measure the deviations from an ideal orbit, and calculate corrections
  Might need to iterate a few times
Beam 1 direction
New sector before correction
After correction

## Slide 25: Beam Collimation and Machine Protection
As beams get more intense, machine protection becomes very important
  Full LHC energy ~ 150 sticks of dynamite!
Beam halo is generally cleaned up through multi-stage collimation

## Slide 26: Secondary Beams
When a proton beam strikes a target, the energy of the beam goes into particle production. Charged particles include (in ~descending order of population)
  p±: Most of the energy
  K±: Charged particles containing a Strange quark
  p: ordinary protons
  e±: These mostly come from neutral pions that immediately decay to two photons.
  Antiprotons:
  Other strange “hyperons”
When and electron beam strikes a target, it makes mostly photons and e±
  Positron production targets can be very efficient.
Generally, we design secondary beam lines to maximize acceptance of the species of beam we’re looking for.

## Slide 27: Special Case: Neutrino Beams
Electron neutrinos are generally produces in nuclear reactors. High energy particle beams are used to produce primarily muon neutrinos in the reactions
Select correct neutrino species by focusing correct pion species
Leading particles

## Slide 28: Neutrino Horns
Neutrino horns work by producing an coaxial current so the correct sign pions are focused in both planes.
This is then followed by a decay region to allow the pions to decay

## Slide 29: Example: MiniBooNE Neutrino Line
(not to scale!)

## Slide 30: Practical Considerations
Neutrino horns operate in fierce radiation environments, and are pulsed with currents of several hundred kA.
They require water cooling and sophisticated mechanical analyses.
Neutrino Horn Assembly at J-Parc

## Slide 31: Antiproton Beams
Antiprotons are produced in very small numbers in proton collisions.
In order to be useful, these must be captured and “cooled” (i.e. have their area in phase space reduced).
Although high energy proton-antiproton colliders are a thing of the past (homework problem), anti-protons are still of great interest at low energy:
  CERN LEAR facility
  FAIR Facility in Germany.

## Slide 32: Highest Intensity Antiproton Source: Fermilab (decommisioned)
120 GeV protons strike a target, producing many things, including antiprotons.
a Lithium lens focuses these particles (a bit)
a bend magnet selects the negative particles around 8 GeV. Everything but antiprotons decays away.
The antiproton ring consists of 2 parts
– the Debuncher – the Accumulator.

## Slide 33: Antiproton Source – debunching
Particles enter with a narrow time spread and broad energy spread.
High (low) energy pbars take more (less) to go around…
…and the RF is phased so they are decelerated (accelerated),
resulting in a narrow energy spread and broad time spread.
At this point, the pBars are transferred to the accumulator, where they are “stacked”

## Slide 34: Stochastic cooling of antiprotons
Positrons will naturally “cool” (approach a small equilibrium emittance) via synchrotron radiation.
Antiprotons must rely on active cooling to be useful in colliders.
Principle: consider a single particle which is off orbit. We can detect its deviation at one point, and correct it at another:
But wait! If we apply this technique to an ensemble of particles, won’t it just act on the centroid of the distribution? Yes, but…
Stochastic cooling relies on “mixing”, the fact that particles of different momenta will slip in time and the sampled combinations will change.
Statistically, the mean displacement will be dominated by the high amplitude particles and over time the distribution will cool.
Simon Van der Meer won the Nobel Prize for this.