## Slide 1: Proton Beam Inter-Bunch Extinction and Extinction Monitoring for the Mu2e Experiment
Eric Prebys, FNAL
HB2012, Beijing, China

## Slide 2: Acknowledgments
Representing the Mu2e Collaboration
  24 Institutions
  ~120 Collaborators
This talk has direct contributions from
  Alexander Drozhdin, FNAL
  Andrei Gaponenko, FNAL
  Carol Johnstone, FNAL
  Vladimir Kashikhin, FNAL
  Peter Kasper, FNAL
  Sasha Makrarov, FNAL
  Bill Molzon, UCI
  Igor Rakhno, FNAL
  Zhengyun You, UCI

## Slide 3: The Physics of Mu2e: m+N  e+N
Nearly all models beyond the Standard Model predict the interaction:
m
105 MeV e-
If captured on the nucleus, a muon will have an enhanced probability of exchanging a virtual neutral particle
  Could be a g or heavy boson.
  Two body decaymono-energetic electron!
Similar to megwith important advantages:
  No combinatorial background
  Because the virtual particle can be a photon or heavy neutral boson, this reaction is sensitive to a broader range of BSM physics
Goal: measure with a single event sensitivity of <10-16

## Slide 4: Experimental Technique and Extinction
A proton beam will be used to create muons, which will be transported and captured on an Aluminum target.
Most backgrounds are prompt with respect to the parent protons, so a pulsed beam will be used.
  Detection window will be after backgrounds have died away
Out of time protons would limit sensitivity and must be suppressed at the 10-10 level (“Extinction”)

## Slide 5: Muon Beam Line and Mu2e Detector
Production Target
  Proton beam strikes target, producing mostly pions
Production Solenoid
  Contains backwards pions/muons and reflects slow forward pions/muons
Transport Solenoid
  Selects low momentum, negative muons
Capture Target, Detector, and Detector Solenoid
  Capture muons on Aluminum target and wait for them to decay
  Detector blind to ordinary (Michel) decays, with E≤½mmc2
  Optimized for E~mmc2

## Slide 6: Overview: Proton Delivery at Fermilab
Booster
Main Injector/Recycler
Delivery Ring (formerly pBar Debuncher)
Mu2e
One Booster batch (4x1012 protons) is injected into the Recycler.
It is divided into 4 bunches of 1012 each
These are extracted one at a time to the Delivery Ring
  Period = 1.7 msec
As a bunch circulates, it is resonantly extracted to produce the desired beam structure.
  Bunches of ~3x107 protons each
  Separated by 1.7 msec

## Slide 7: Extinction Systems
Extinction will be achieved in two phases:
  In ring
    Beam delivery technique automatically gives good extinction < 10-5 going into the Delivery Ring
    May degrade to 10-4 during the spill
  In beam line
    System of AC dipoles and collimators
    Factor of 10-7 should be possible
Monitoring
  Need to show that 10-10 has been achieved

## Slide 8: Delivery Ring
Start with < 10-5 level of extinction going into the Delivery Ring, so the issue is how will it grow during the spill.
Effects considered
  RF noise
  Intrabeam scattering
  Beam loading
  Beam-gas interaction
  Scattering off of extraction septum
Simulation still ongoing, but it looks like it should be possible to maintain a 10-5 level of extinction.

## Slide 9: Extinction on the Proton Beam Line
The proton delivery beam line will contain a system of resonant dipoles (“AC dipoles”) and collimators to eliminate out of time beam
Delivery Ring
Proton Beam Line
Mu2e Experiment

## Slide 10: Generic Beamline Extinction Analysis
Beam fully extinguished when deflection equals twice full admittance (A) amplitude
At collimator:
Angle to extinguish beam:
Assumptions:
Beam occupies entire admittance
Beam line admittance is equal to the collimation channel’s admittance
Resonant dipole that deflects out-of-time beam into a collimation system
At dipole:

## Slide 11: Magnet Considerations
Bend strength to extinguish:
Stored Energy:
Large bx, long weak magnets
- Assume bx=250m, L=6m
- Factor of 4 better than bx=50m, L=2m

## Slide 12: Features of the Extinction Beam Line
Upstream of extinction dipole
  Collimation to define beam line admittance to 50 p-mm-mr
AC dipole region
  Bend plane: b=250m
  Non-bend plane: waist
Extinction collimation
  Minimize transmission of scraping particles
Post-extinction
  High dispersion region for momentum collimation.

## Slide 13: Wave Forms Analyzed
Of the options considered:
½ harmonic – (2/17) * 17/2 harmonic seems most promising
Bunch length
Transmission window

## Slide 14: Wave Form Optimization
Transmission efficiency was simulated with more realistic bunch shapes
  Harmonic number and amplitude of high frequency component was varied
This study produced in the final parameters for the two harmonic system
Beam motion in Collimator
Transmission Window
Bunch

## Slide 15: AC Dipole Prototype*
1 .5m prototype has built and tested
  Successfully operated at both frequencies
Plan is to build final system out of identical 1m segments
Gap
Cooling channel
Conductor
Ferrite
*Design by Sasha Makarov and Vladimir Kashikhin

## Slide 16: Extinction Simulation
The extinction beam line was simulated using STRUCT and MARS*
Time (ns)
Extinction Region
Collimator Material:
Extinction < 5x10-8 over range of interest for optimized collimators
This is multiplied by the Delivery Ring factor to produce a total extinction of < 5x10-12
*I. Rakhno

## Slide 17: Monitor Requirements
Demonstrate 10-10 extinction
  Assume ≈ 3 x 107 protons/bunch
  Not possible measure 10-10 with a single bunch
     Integrate over many bunches
  Integration time should be < ≈ 1 hour
Only protons hitting the target can cause backgrounds
  Monitoring beam itself will lead to a potentially large over estimate of the background to the experiment
   Monitor target interaction product and integrate a statistical profile of out of time beam.

## Slide 18: Statistical Filter + Detector Strategy
Filter
  Selects a sample of suitable secondaries and delivers them to the detector
  Sets the per proton detector signal rate
  Shields the detector from unwanted interaction products
Detector
  Measure “in-time” and “out-of-time” signal rates with equal or known relative efficiency
  Must have LOW “out-of-time” backgrounds compared to signal rate

## Slide 19: Precision Monitor Options
Pixel Tracker
  Located above and behind the proton absorber
  Samples 3 to 4 GeV/c positive charged secondaries
  Pixel detectors reconstruct and count straight tracks with a well defined direction in 25ns time bins
Mini Spectrometer
  Located beside the proton absorber
  Samples ~ 1 GeV/c positive charged secondaries
  Magnetic spectrometer with 4 scintillator stations measures dE/dx, time of flight, and momentum of identified particle tracks

## Slide 20: Requirements
Signal Rate
  Determined from beam intensity
    3 x 107 protons/bunch
    Bunch rate: 0.6 MHz @ 33% duty factor
     2 x 1016 in-time p.o.t./hr
    10-10 extinction  2 x 106 out-of-time p.o.t./hr
  To set a 90% C.L.
    Need 2.3 expected out-of-time signal/hr
     1.2 x 10-6 signal events per p.o.t.
Background
  << 1 event/hr
Both approaches seem to satisfy these requirements
  Down selection committee formed.
  Recommendation in November

## Slide 21: What’s Next
In ring extinction
  Complete calculations and simulations to determine the likely level of out of time beam.
  Work in mitigation, such as in ring momentum collimation, if it’s insufficient.
Beam line extinction
  Magnet design appears sound
  Continue modeling effort to optimize collimation design.
Monitoring
  Down select between two precision monitor options
  Develop fast monitor to measure extinction at the 10-5 level monitor beam coming out of the ring before the AC dipole
    Hope to combine with precision intensity measurement for slow extraction feedback.

## Slide 22: Mu2e Schedule

## Slide 23: Conclusions
Extinction and extinction monitoring are a critical part of the Mu2e schedule
We have developed a plan for beam line extinction and have two apparently viable options for precision monitoring
More analysis is required to determine what, if any, further mitigation will be required in Delivery Ring to achieve the required 10-5 level of extinction.