## Slide 1: Status and Plans for LARP Eric Prebys (outgoing) LARP Director

## Slide 2: LARP History
The US LHC Accelerator Research Program (LARP) was formed in 2003 to coordinate US R&D related to the LHC accelerator and injector chain at Fermilab, Brookhaven, and Berkeley
  SLAC joined shortly thereafter
  Has also had some involvement with Jefferson Lab, Old Dominion University and UT Austin
LARP has contributed to the initial operation of the LHC, but much of the program is focused on future upgrades.
The program is currently funded at a level of about $12-13M/year, divided among.
  Accelerator research
  Magnet research (~half of program)
  Programmatic activities, including support for personnel at CERN

## Slide 3: Some (random) LARP Activities
Personnel support (to date):
  11 Toohig Fellows
    Postdoctoral Fellows who divide time between CERN and LARP host lab
  8 Long term visitors
    Senior personnel spending between 6 months and two years at CERN.
Flat Bunches
AC Dipole
Sync. Light Monitor
Luminosity Monitor
Instability Modeling
Crystal Channeling
Rotatable Collimators

## Slide 4: Impact of LARP Personnel Programs
Letter to Michael Procario, Acting Head, DOE Office of High Energy Physics, 9-MARCH-2011
(…)

## Slide 5: Relevance of LARP to CERN Upgrade*
(…)
Letter to Dennis Kovar, Head, DOE Office of High Energy Physics, 17-August-2010

## Slide 6: Context: LHC Upgrade Path
Time Line:
  LS1*: “Nominal” (2013-2014)
    Complete repairs of the superconducting joint and pressure relief problems which cause “the incident” in 2008 and currently limit the energy to 4+4 TeV.
    “Lost memory” issues may limit the beam energy to somewhere between 6.5 and 7 TeV per beam.
    At least 1x1034 cm-2s-1 peak luminosity
  LS2: “Ultimate” (2017)
    injector and collimation upgrades
    At least 2x1034 cm-2s-1 peak luminosity
  LS3: “HL-LHC” (~2022-2023)
    Lower b* and compensate for crossing angle to maximize luminosity
    5x1034 cm-2s-1 leveled luminosity
*LS = “Long Shutdown”

## Slide 7: LARP Magnet Development Tree
Completed
Achieved
220 T/m
Being tested
Length scale-up
High field
Accelerator features

## Slide 8: Recent Success!
120 mm aperture x 1 m HQ reached 170 T/m at FNAL
It was agreed with CERN that this would establish Nb3Sn as a viable technology for the LHC upgrade
Next step is a real prototype.
Press release coming soon.

## Slide 9: New Direction for LARP
LARP has historically been an R&D organization
  Not well structured for hard deliverables
  CERN upgrade plans in a state of flux
Recent developments
  CERN has formalized the planning for the luminosity upgrade
  In June 2012, CERN chose 150 mm as the aperture for the final focus quads
At the DOE’s request, we are in the process of transforming LARP into a project to encompass all US contributions to the luminosity upgrade of the LHC.
Budget Guidance
  Flat-Flat LARP funding @ ~$12.4M/year through FY16
  A total of $200M (then year dollars) TPC, assuming CD-3 at approximately the beginning of FY17
  “Some amount” of General Accelerator Research and Development (GARD) funds invested in support of this program.

## Slide 10: Candidate Deliverables Considered
Traditional LARP Scope
  150 mm aperture Nb3Sn quadrupoles
    Likely just cold masses, divided between here and CERN
  Crab Cavities
    Prototypes. Production Units. Cryomodules.
  High Bandwidth Feedback System
    Pick-ups. Processing Systems. Response Kickers.
  Collimation
    Rotatable collimators.
    Hollow electron beams.
New Scope
  11 T Nb3Sn dipoles
    Used to make room for collimation in dispersion suppression region
    Has been a bilateral CERN/FNAL effort
  Large Aperture NbTi D2 separator magnets
    First dual aperture magnets near Irs
    Has been bilateral CERN/BNL effort

## Slide 11: Proposed Deliverables
A consensus quickly emerged among scope selection committee (CERN, DOE, LARP labs) regarding priority
  Core deliverables
    Magnets:
      US will deliver half of Nb3Sn cold masses for final focus magnets at ATLAS and CMS IPs
      CERN will collaborate on the prototype and proved the other half of the cold masses, as well as cryostats and all infrastructure.
    Crab cavities:
      US will produce cavities to test in the SPS in 2016
      US will build crab cavities and cryomodules for luminosity upgrade.
      CERN will provide power couplers, power supplies, cryo, and infrastructure.
    Feedback:
      US will provide algorithms, processing hardware/firmware, and RF components for a functioning feedback system in the SPS.
      CERN will provide vacuum components (pickups and kickers).

## Slide 12: Status and Plans
We presented the rough plan to the DOE in February, 2013
  Generally supportive of proposed deliverables and required funding profile.
  Moved forward with planning
Internal review of deliverables in June 2013,
  Positive about projects and level of planning
  Some concern about early funding requirements for crab cavities
Currently revising management structure more appropriate to a large project with hard deliverables.
  Giorgio Apollinari chosen as new LARP Director!

## Slide 13: Traditional LARP Structure

## Slide 14: Proposed New Structure
Traditional LARP

## Slide 15: Conclusion
LARP has been extremely successful at leveraging US capabilities to develop technology for the LHC.
We are in the process of transforming the program into a production effort to produce significant hard deliverables for the LHC luminosity upgrade.
Big thanks for all the hard work from all of the people involved and for the support of our collaborators at CERN!

## Slide 16: BACKUP Material

## Slide 17: LARP Contributions to Current LHC Operation
Schottky detector
  Used for non-perturbative tune measurements (+chromaticities, momentum spread and transverse emmitances) – Operational (currently some issues)
Tune tracking
  Implement a PLL with pick-ups and quads to lock LHC tune – Fully integrated
  Investigating generalization to chromaticity tracking
AC dipole
  US AC dipole to drive beam
  Measure both linear and non-linear beam optics – Primary tool for high energy optics
Luminosity monitor
  High radiation ionization detector integrated with the LHC neutral beam absorber (TAN) at IP 1 and 5. – Functional, becoming primary fast system.
Synchrotron Light Monitor
  Used to passively measure transverse beam size and monitor abort gap
  Not a LARP project, but significantly improved by LARP – Operational (currently some issues)
Low level RF tools
  Leverage SLAC expertise for in situ characterization of RF cavities – Fully integrated
Personnel Programs
  Toohig postdoctoral fellowship
  Long Term Visitor Program

## Slide 18: Motivation: The Big Picture
3000 fb-1
~ 50 years at nominal LHC luminosity!
The future begins now

## Slide 19: HiLumi-LHC Design Study
The Luminosity upgrade planning will be largely organized through EU,
  Centrally managed from CERN (Lucio Rossi and Oliver Bruning)
  Non-CERN funds provided by EU
  Non-EU partners (KEK, LARP, etc) will be coordinated by HiLumi-LHC, but receive no money.
Work Packages:
  WP1: Management
  WP2: Beam Physics and Layout
  WP3: Magnet Design
  WP4: Crab Cavity Design
  WP5: Collimation and Beam Losses
  WP6: Machine Protection
  WP7: Machine/Experiment Interface
  WP8: Environment & Safety
LARP is now integrating most of its activities into this framework
  Two LARP meetings/year two joint meetings/year (spring in US, fall in Europe)
Goal
  CDR: 2014
  TDR: 2015
Significant LARP and other US Involvement

## Slide 20: Key Components of HL-LHC
Reduce b* from 55 cm to 15 cm
  Requires large aperture final focus quads
  Beyond NbTi without making the quads unmanageably long.
  Requires Nb3Sn
    never before used in an accelerator!
    Nb3Sn R&D key component of LARP
BUT, reducing b* increases the effect of crossing angle
“Piwinski Angle”

## Slide 21: (Rough) Budget Assumptions
“Traditional” LARP funding
  Flat-flat @ $12.4M/year through FY16
    $9.4M for these projects and related management
      =$37.6M
    $3M for continuing R&D which is not included here
Project Funding
  $200M
    Nominally starting in FY17
    Some funds available for procurement and infrastructure as early as FY15
Significant GARD and CERN contributions will not be represented by specific dollar amounts at this point, but rather as assumptions about what will be contributed from outside the project and therefore will not appear in our budget
  Clearly, this will have to be formalized at some point

## Slide 22: The Process
Committee formed consisting of
  LARP Management
    Eric Prebys, FNAL
    Tom Markiewicz, SLAC GianLuca Sabbi, LBNL
    Peter Wanderer, BNL
  CERN HL-
    Lucio Rossi, CERN
    Oliver Brüning, CERN
  DOE
    Bruce Strauss, DOE
  Labs
    Represented by Stuart Henderson, FNAL
  Project support
    Marc Kaducak, FNAL
Met several times over several weeks, including at the fall meeting in Frascati

## Slide 23: Feedback from CERN
Top Priority
Backup

## Slide 24: Proposed Magnet Contribution
In June, 2012, the choice was made of 150 mm as the aperture for the focusing quads in the LHC upgrade.
LARP activities have been modified in accordance with this decision and recommendations of our July 2012 review
  Curtail existing 120 mm program
  Work with CERN to develop a 150 mm prototype (LQXF)
The program will then full transition into a production project to produce the focusing quadrupoles for the LHC upgrade
  US contribution
    Cold masses for the Q1 and Q3 quads, to be cryostated at CERN
    A total of 20 half length (4 m) cold masses, including 2 pre-series units, 16 production units, and 2 spares

## Slide 25: Crab Cavity Development

## Slide 26: Proposed Crab Cavity Contribution
LARP has been a major proponent of crab cavities since the beginning
  Currently two of the three candidate designs are from within LARP
Crab cavities leverage US expertise and US industry
  All prototypes, including the UK prototype, have been built in the US.
Proposal
  The LARP R&D program will continue work on the two cavity designs:
    RF-Dipole
    Double Quarter Wave
  Efforts will increase at FNAL on cryostat design
  This will culminate with the delivery of a test cryostat with cavities of one of the designs for a beam test in the SPS (2015 or 2016)
  The project will undertake the production of 10 cryomodules (4 per IP + 2 spares) for installation in the LHC upgrade
    CERN will provide RF couplers and all required infrastructure

## Slide 27: Feedback System

## Slide 28: High Bandwidth Feedback System
The high bandwidth feedback system is a proposed feedback system for the SPS, which leverages LARP experience with the LHC LLRF system
Proposal
  LARP will continue R&D related to the system.
  The deliverable would be a functional feedback system the SPS, for which
    The US contribution would be the complete, full-function, instability control system hardware, firmware and software necessary to operate at the SPS (and potentially LHC, PS).
    The CERN contribution will include the vacuum structures (pickup(s) and kicker(s)) and all tunnel related cable plant.