## Slide 1: Fermilab Accelerator Science and Technology (FAST) Facility
Eric Prebys
Accelerator Physics Center
Fermilab

## Slide 2: A Brief History of Fermilab (evolving slide)
  1968: construction begins
  1972: first beams
    200400 GeV proton beams
    Highest energy lab ever since
  ~1985:
    “Tevatron”: first superconducting synchrotron.
    900GeV x 900 GeV p-pBar collisions
  Upgraded in 1997
    Main Injector-> more intensity
    980 GeV x 980 GeV p-pBar collisions
    Intense neutrino program
  Soon the second most powerful collider
  Fermilab is now the only remaining US High Energy Physics Lab
  With the LHC now the highest energy collider, the lab must focus on different types of physics.
until recently
For awhile

## Slide 3: Fermilab Firsts and Records
Firsts:
  First separated function synchrotron:
    Main Ring, 1972
  First superconducting synchrotron/collider
    Tevatron, 1983 (first collisions in 1986)
  First permanent magnet storage ring
    Recycler, 2000
Records:
  Highest energy proton beam
    Main Ring, 1972 (breaks AGS record)1983 (broken by Tevatron)
    Tevatron, 1983-2008 (broken by LHC)
  Highest energy hadron collider
    Tevatron, 1986 (breaks SppS record)2009 (broken by LHC)
  Highest hadronic luminosity
    Tevatron, 2005 (broke ISR *p-p* record!)  2011 (broken by LHC)
  Highest energy p-pbar collider
    Tevatron, 1986 (breaks SppS record) present
  Highest p-pbar luminosity
    Tevatron, 1992 (broke SppS record) present

## Slide 4: Context: P5 Report
The “Particle Physics Project Prioritization Panel” (P5) advises the DOE Office of High Energy Physics on research funding priorities in high energy physics
After a lengthy process, the panel released a report in May, 2014. Top priorities for Fermilab:
  Support the LHC and its planned luminosity upgrades
  Pursue the g-2 and Mu2e muon programs*
  Focus on a high energy neutrino program to determine the mass hierarchy and measure CP violation.
    “Flagship” activity
    Will ultimately require a “multi-megawatt” beam at 60-120 GeV
  Continue at least R&D toward a future linear e+e- collider (ILC)
*E. Prebys, UCD Colloquium, March 28, 2016
FAST supports these

## Slide 5: ILC-Related R&D
This is the easy one…
Over the last ~15 years, Fermilab has gone from having no SRF program to becoming one of the world leaders.
Fermilab areas of interest include
  Increasing gradient and high-gradient-Q of cavities
  Source/LEBT/RFQ/MEBT development
  Bunch manipulation
  Systems and integration issues.
This work is largely orthogonal to the rest of the Fermilab program
Understanding the rest of the program requires some understanding of the lab’s long term plans…
FAST program

## Slide 6: Orientation: Accelerator Complex
Following the LHC turn-on, FNAL has transitioned to an intensity based program
Intensities are limited by the 8 GeV proton source, which is still largely original.
/400 MeV
/8 GeV
120 GeV+secondaries
Recycler: Formerly for pBar storage, now to “pre-stack” protons for the Main Injector
Accumulator/Debuncher: Formerly for pBar accumulation, re-tasked for muon program.
Neutrinos
~45 years old!
LBNF
(120 GeV)

## Slide 7: Current Long Baseline n Program
The “Neutrinos from the Main Injector” (NuMI) line uses 120 GeV neutrinos from the Main Injector to produce neutrinos, which are detected in
  MINOS: 725 km away
  NOnA: 810 km, 14.6 mrad off axis
    Produces narrower energy spread, which is important for physics goals

## Slide 8: Future n Program: LBNFDUNE
Fermilab will construct a new new “Long Baseline Neutrino Facility” (LBNF) beam line to produce neutrinos for the “Deep Underground Neutrino Experiment” (DUNE), located at the “Sanford Underground Research Facility” (SURF) in Lead, SD, 1300 km away.
Truly international effort, including 150 institutions in 27 countries.
Physics program extends 20-30 years.

## Slide 9: Critical Issue: Space Charge Limit
The maximum useful injected charge into the Booster is limited by the space charge tune-shift, which can drive harmonic instabilities.
So the maximum accelerated charge grows rapidly with increasing energy
Could gain an additional factor of bg if we were not constrained by the MI admittance
total protons
normalized emittance
“Bunch factor” = Ipeak/Iave
(Reduce with higher RF harmonics)
= 3 for 95% Gaussian emittance
1 for 100% uniform (painted) emittance
doesn’t include improvement of going to uniform distribution with painting

## Slide 10: Staged Plan to Increase Intensity
Proton Improvement Plan (PIP) (ongoing)
  Numerous improvements to maximize potential of existing complex.
  Provide 700 kW to NuMI + 30 kW to 8 GeV program
PIP-II (CD-0)
  Keep existing Booster, but increase cycle rate from 15 to 20 Hz
  Replace existing 400 MeV linac with 800 MeV superconducting linac that has CW capability
  Deliver 1.2 MW to NuMI or LBNF
  Support 8 GeV program and 800 MeV program
    (eg. 100kW 800 MeV beam to Mu2e-II)
PIP-III (conceptual)
  Keep PIP-II linac
  Replace Booster with “something”
  Deliver 2.5 MW to LBNF + ??
Rapid Cycling Synchrotron (RCS) or pulsed linac?

## Slide 11: PIP-II R&D
The PIP-II Injector Experiment (PXIE) is designed to test the technology needed for the PIP-II Linac
Among other things, PXIE will investigate
  Low Energy Beam Transport (LEBT) pre-chopping.
  Validation of chopper performance
  Bunch extinction
  Operation of Half Wave Resonator (HWR) in close proximity to 10 kW absorber
  Emittance preservation
FAST/IOTA
PXIE
What I’ll be talking about

## Slide 12: Beyond PIP-II: Linac vs. RCS
The linac option would provide more beam at 8 GeV or lower energies, which could support a very diverse physics program, however
Unless there is a major breakthrough in SRF technology, it would cost significantly more than the RCS option.
The strong feedback from the DOE is that we should pursue the most cost effective way to deliver high power beam to LBNF/DUNE, with no specific mandate for a lower energy program. Therefore…
We are pursuing the rapid cycling synchrotron as the primary option, with the linac as backup
  There might be a breakthrough in SRF technology
  Priorities have been known to change

## Slide 13: PIP-III Straw Man Parameters*
~6x record Booster protons per pulse
~4x record Main Injector protons per pulse
*P. Derwent

## Slide 14: Mitigating Space Charge in Synchrotron
Recall:
Other ways?
  This is where FAST comes in!
Can paint beam to increase emittance, but limited by Main Injector aperture (~20-25 p-mm-mr)
Can increase injection energy (costly)

## Slide 15: RCS Comparisons
Too big for “ordinary” synchrotron. Can FAST help?
2.5 MW @ 60 GeV
We’d rather not build the expensive linac extension if we don’t have to

## Slide 16: What are “Nonlinear Integrable Optics”?
All accelerators today are based on physics worked out in the 1950s
  Stable orbits based on “linear” optics
    The defining magnetic lattice contains only dipole and quadrupole terms.
    The result is a system in which particles experience a transverse force which depends linearly on their deviation from a reference orbit. Described in general by a “Hill’s Equation”

## Slide 17: Interesting Footnote
Strong focusing was actually previously invented by a Greek elevator engineer named Nicholas Christofilos, who applied for a patent in 1950.
After they became aware of if, Courant and Snyder recognized the priority of Christofilos’ work in their 1958 paper, which lays the groundwork for all synchrotrons built to this day.

## Slide 18: All the Accelerator Physics U Need 2 Know
We can describe (strongly focused) particle motion in terms of initial conditions and a “beta function” β(s), which is only a function of location along the nominal path, and follows the periodicity of the machine.
In other words, particles undergo “pseudo-harmonic” motion about the nominal trajectory, with a variable wavelength.
Note: β has units of [length], so the amplitude has units of [length]1/2
The “betatron function” β(s) is effectively the local wavenumber and also defines the beam envelope.
Phase advance
Lateral deviation in one plane
s
x

## Slide 19: Formalism: Coordinates and Conventions
We generally work in a right-handed coordinate system with x horizontal, y vertical, and s along the nominal trajectory (x=y=0).
Particle trajectory defined at any point in s by location in x,x’ or y,y’ “phase space”
unique initial phase space point  unique trajectory
Note: s (rather than t) is the independent variable

## Slide 20: Transfer Matrices
Dipoles define the trajectory, so the simplest magnetic “lattice” consists of quadrupoles and the spaces in between them (drifts). We can express each of these as a linear operation in phase space.
By combining these elements, we can represent an arbitrarily complex ring or line as the product of matrices.
Quadrupole:
Drift:

## Slide 21: Hamiltonian Treatment of Accelerators
Like other mechanical systems, accelerators are treated with Hamiltonian formalism. For a simple system, the Hamiltonian I given by:

## Slide 22: Motion in a Linear System
Properties of linear lattices
  Explicit solution
  In the paraxial approximation (sinq~tanq~q), particles undergo a fixed number of oscillations per orbit (“tune”) which is independent of amplitude.
Nonlinear terms are dealt with perturbatively, and generally lead to chaotic instability at high amplitudes
octupole

## Slide 23: Betatron Tune
As particles go around a ring, they will undergo a number of betatrons oscillations ν (sometimes Q) given by
This is referred to as the “tune”
We can generally think of the tune in two parts:
Ideal orbit
Particle trajectory
6.7
Integer : magnet/aperture optimization
Fraction: Beam Stability

## Slide 24: Instabilities In Linear Systems
A unique tune leads to inherent instabilities
  Tune spread”Landau Damping”
Lattice imperfections lead to harmonic instabilities
In particular, space charge can shift the tune onto an instability
  Space charge limit

## Slide 25: Do Accelerators Need to be Linear?
Motion will be stable if we can identify conserved integrals of motion”Integrable”
There has been a long search for integrable nonlinear systems.
Early work
  Orlov (1963)
  McMillan (1967) – 1D solution
  Perevedentsev, Danilov (1990) – generalization of McMillan case to 2D, round colliding beams. Require non-Laplacian potentials to realize

## Slide 26: 2D Generalization of McMillan Mapping
1D – thin lens kick
2D – a thin lens solution can be carried over to 2D case in axially symmetric system (non-Laplacian!)
1. The ring with transfer matrix
2. Axially-symmetric thin kick

## Slide 27: 2D Generalization of McMillan Mapping
The system is integrable. Two integrals of motion (transverse):
  Angular momentum:
  McMillan-type integral, quadratic in momentum
For large amplitudes, the fractional tune is 0.25
For small amplitude, the electron (defocusing) lens can give a tune shift of ~ –0.3 per cell !
Potentially, can cross an integer resonance

## Slide 28: Verification: VEPP-2000
Danilov and Perevedentsev’s “round colliding beams”
  equal beta functions, tunes, and emittances
  no coupling
Under these conditions
  longitudinal component of angular momentum is conserved
  dynamics is “quasi integrable”
This was demonstrated experimentally at the BINP VEPP-2000 e+ e- collider, which achieved record tune spread of 0.25 (Romanov, NA-PAC13)
Solution would be fully integrable if beams had “McMillan distribution”
  Can also be achieved with electron lenses!

## Slide 29: We can test this: IOTA Electron Lens
Capitalize on the Tevatron experience and recent LARP work
Re-use Tevatron EL components
Arbitrary current profile

## Slide 30: Laplacian Solution*
Start with a Hamiltonian
Choose s-dependence of the nonlinear potential such that H is time-independent in normalized variables
This results in H being the integral of motion
Note: there is no requirement on V – can be made with any conventional magnets, i.e. octupoles
*Danilov and Nagaitsev, Phys. Rev. ST Accel. Beams 13, 084002 (2010) (2010)

## Slide 31: Nonlinear Integrable Optics with Laplacian Potential*
Start with a round axially-symmetric linear lattice (FOFO) with the element of periodicity consisting of
  Drift L
  Axially-symmetric
  focusing block “T-insert”
  with phase advance n×p
Add special nonlinear potential V(x,y,s) in the drift such that
can be also

## Slide 32: Stability of Nonlinear Lattices
Nonlinear systems can be more stable!
1D systems: non-linear (unharmonic) oscillations can remain stable under the influence of periodic external force perturbation. Example:
2D: The resonant conditions
are valid only for certain amplitudes; i.e. the tune depends on the initial conditions!
Nekhoroshev’s condition guaranties detuning from resonance and, thus, stability.
  An Exponential Estimate of the Time of Stability of Nearly-Integrable Hamiltonian Systems. Russian Math. Surveys 32:6 (1977) from Uspekhi Mat. Nauk 32:6 (1977)
Notes: change ref.

## Slide 33: Space Charge in Linear Optics
System: linear FOFO 100 A linear KV w/mismatch
Result: quickly drives test-particles into the halo
Tech-X, RadiaSoft simulation
DQsc ~ –0.7

## Slide 34: Space Charge in NL Integrable Optics
System: linear FOFO 100 A linear KV w/mismatch
Result: nonlinear decoherence suppresses halo
Tech-X, RadiaSoft simulation
DQsc ~ –0.7

## Slide 35: Studies at Fermilab: FAST/IOTA
The former New Muon Lab (NML) was originally being developed as an R&D facility for the ILC.
  Original plan was for three ILC cryomodules.
This evolved into a plan for an electron-based study program.
DOE reviews concluded that there are numerous electron-based facilities in the country, but that the IOTA portion was unique.
On their recommendation, the priorities of the facility were modified to focus on the IOTA ring.
  Primary purpose for the electron beam is as an injector
  Will also support an ancillary R&D program.

## Slide 36: Current Plan for FAST/IOTA
Because the emphasis of the facility has changed, so has had the name: ASTA/IOTAFermilab Accelerator Science and Technology (FAST) Facility
  Reduce cryomodules from three to one
  Primary mission is as an injector for IOTA

## Slide 37: e- Injector
Parameter | ILC nominal | Range
Bunch charge | 3.2 nC | 10pC to > 20 nC
Bunch spacing | 333 ns | <10 ns to 10 s
Bunch train | 1 ms | 1 bunch to 1 ms
Train rep. rate | 5 Hz | 0.1 Hz to 5 Hz
Transverse emit. | 25 mm-mrad | 1 to 100 mm-mrad
r.m.s. bunch length | 1 ps | 10fs to 10ps
Beam energy | 300 MeV | 50-300 MeV

## Slide 38: ASTA
Progress
  Electron source and cryomodule are in place
  First 50 MeV electron beam

## Slide 39: First Electrons Through Photoinjector!
Sign-offs Wednesday, 25 March, 2015
Electrons beyond the gun - Wednesday, 25 March
Beam after CC2, towards end of line – Thursday, 26 March
Electrons seen at low energy beam absorber ( ~20 MeV) – Friday morning, 27 March

## Slide 40: Validating Nonlinear Optics
Both electron lenses and nonlinear magnetic elements involve discrete insertions in an otherwise conventional lattice.
  Albeit a lattice with strict control over lattice functions!
This allows for the design of a fairly simple “test bed” to evaluate the efficacy of these solutions.

## Slide 41: Integrable Optics Test Accelerator (IOTA)
e- beam line
2.5 MeV RFQ
p beam line

## Slide 42: IOTA Layout

## Slide 43: IOTA Parameters (Electrons)
Nominal kinetic energy | e-: 150 MeV
Nominal intensity | e-: 1×109
Circumference | 40 m
Bending dipole field | 0.7 T
Beam pipe aperture | 50 mm dia.
Maximum b-function (x,y) | 12, 5 m
Momentum compaction | 0.02 - 0.1
Betatron tune (integer) | 3 - 5
Natural chromaticity | -5 - -10
Transverse emittance r.m.s. | 0.04 mm
SR damping time | 0.6s (5×106 turns)
RF V,f,h | 1 kV, 30 MHz, 4
Synchrotron tune | 0.002 - 0.005
Bunch length, momentum spread | 12 cm, 1.4×10-4

## Slide 44: Nonlinear Magnet
Joint effort with RadiaBeam Technologies (Phase I and II SBIR)
FNAL Concept: 2-m long
nonlinear magnet
RadiaBeam short prototype. The full 2-m magnet will be designed, fabricated and delivered to IOTA in Phase II

## Slide 45: IOTA Goals for Integrable Optics
The IOTA experiment has the goal to demonstrate the possibility to implement nonlinear integrable optics with a large betatron frequency spread DQ>1 and stable particle motion in a realistic accelerator design
Benefits of nonlinear integrable optics include
Increased Landau damping
Improved stability to perturbations
Resonance detuning

## Slide 46: Integrable Optics Test Accelerator (IOTA)
Unique features:
  Can operate with either electrons or protons (up to 150 MeV/c momentum)
  Large aperture
  Significant flexibility of the lattice
  Precise control of the optics quality and stability
  Set up for very high intensity operation (with protons)
Based on conventional technology (magnets, RF)
Cost-effective solution
  Balance between low energy (low cost) and discovery potential

## Slide 47: IOTA Staging – Phase I
Phase I will concentrate on the academic aspect of single-particle motion stability using e- beams
  Achieve large nonlinear tune shift/spread without degradation of dynamic aperture by “painting” the accelerator aperture with a “pencil” beam
  Suppress strong lattice resonances = cross the integer resonance by part of the beam without intensity loss
  Investigate stability of nonlinear systems to perturbations, develop practical designs of nonlinear magnets
  The measure of success will be the achievement of high nonlinear tune shift = 0.25
Notes: color pencil beam

## Slide 48: IOTA Staging – Phase I
The magnet quality, optics stability, instrumentation system and optics measurement techniques must be of highest standards in order to meet the requirements for integrable optics
  1% or better measurement and control of b-function, and 0.001 or better control of betatron phase
This is why Phase I needs pencil e- beams as such optics parameters are not immediately reachable in a small ring operating with protons

## Slide 49: Experimental Procedure
Two kickers, horizontal and vertical, place particles at arbitrary points in phase space
Measure beam position on every
turn to create a Poincare map
As electrons lose energy due to synchrotron radiation, they will cover all available phase space
Can control the strength on the nonlinearity
Final goal – measure dependence of betatron frequency on amplitude

## Slide 50: Phase II: Proton Injection
Luckily, we have an extra RFQ just lying around…
The HINS (“High Intensity Neutrino Source”) was developed as the front end of a pulsed “Project X” 8 GeV proton linac
Because of cooling problems, it never reached its design pulse rate
ProjectX (now PIP-II) specification was changed to a CW front end
  HINS->PXIE
HINS RFQ available for our use

## Slide 51: IOTA Proton Injector Parameters

## Slide 52: Phase II (cont’d)
After the IOTA commissioning, we will move the existing 2.5 MeV proton/H- RFQ into the FAST hall to inject protons into the IOTA ring.
Allows tests of Integrable Optics with protons and realistic space charge beam dynamics studies
Allows space charge compensation experiments
Unique capability
2.5 MeV RFQ
DQSC =0.5 for one-turn injection
*multi-turn injection possible
Notes: multi-tun injection possible

## Slide 53: Space Charge Compensation
B=E
r, across the beam

## Slide 54: Plan of Activities and Status
Phase 1: FY15-17
Construction of main elements of the FAST/IOTA facility:
  electron injector based on existing FAST electron linac
    Low energy injector operational. HE beamline construction in FY15. Connect CM2 and send beam down HE beamline in FY16
  IOTA ring
    Most components procured. Begin assembly in FY16
  proton injector based on existing HINS proton source in situ
    Resurrecting the ion source in FY15, RFQ in FY16
  special equipment for AARD experiments.
Commissioning of the IOTA ring with electron beam – FY17
Study of single-particle dynamics in integrable optics with electron beams.

## Slide 55: Plan of Activities – Outlook
Phase 2: FY18-20
Commission IOTA operation with proton beams.
Carry out space-charge compensation experiments with nonlinear optics and electron lenses.
Phase 3: FY21 and beyond
Study the application of space-charge compensation techniques to next generation high intensity machines.
Expand the program beyond these high priority goals to allow Fermilab scientists and a broader accelerator HEP community to utilize unique proton and electron beam capabilities of the FAST/IOTA facility

## Slide 56: Open Questions
Instrumentation:
  Loss monitors:
    Protons don’t get out of beam pipe!
    Tentatively chosen diamond-based loss monitors in vacuum
  Transverse proton development
    Ionization Profile Monitor?
    Gas jet?
    Electron Deflection?
    One of these plus retractable loss monitors for tails
Experimental program:
  Fermilab has R&D has always been very “mission-oriented”
  No real experience with a general purpose accelerator physics facility

## Slide 57: Collaboration
A lot of interest to participate in IOTA from the accelerator community
  2 annual Collaboration Meetings, ~60 participants
  ‘IOTA Focused Workshop’
Significant intellectual and in-kind contributions, expressions of interest
  NIU, UMD, RadiaSoft, CERN, ORNL, BINP, Colorado State, Univ. Mexico – integrable optics, space charge effects, phase space manipulation
  LBNL, ANL – optical stochastic cooling demonstration
  UMD – multi-pickup beam profile monitor for IOTA
  JINR – integrable optics and space charge, contributed quadrupole magnets for IOTA
  Univ. Frankfurt – electron lens

## Slide 58: International Space Charge Collaboration at IOTA
Collaborating institutions (at present): Fermilab, ORNL, CERN, RadiaSoft, UMD
Work on the scientific case, hardware development, simulations, planning and execution of space charge compensation experiments with protons in IOTA
Major topics
  Operation of IOTA with protons, injection, and space charge measurements
  Space charge compensation in nonlinear integrable lattice
  Special magnets
  Electron lens
  Space charge compensation with electron columns
  Space charge suppression with circular modes – for FCC

## Slide 59: Training and University Collaboration
Excellent connection to the university community through the Joint Fermilab/University PhD program
  Already 9 graduate students doing thesis research at FAST/IOTA
    7 NIU, 1 U.Chicago, 1 IIT, 2 more to join soon
Partnership with university groups
  NIU – DOE GARD grant on OSC
  Univ. of Maryland – NSF grant for IOTA-related work
  Univ. Frankfurt – IOTA electron lens
  Univ. Mexico – ASTA linac commissioning
  Colorado State – ASTA gun stability
  Interest from: UC Berkeley, MIT, Oxford

## Slide 60: Summary
Experimental accelerator R&D at IOTA is one of the cornerstones of the proposed national R&D thrust “Multi-MW Beams and Targets”, and is well aligned with P5 priorities
IOTA offers a unique scientific program aiming at breakthrough research to allow for x3-5 increase of beam intensity in future proton rings
  IOTA augments the US program lacking ring facilities for accelerator research and training
IOTA experiments are a great opportunity to explore something truly novel with circular accelerators
IOTA will be a strong driver of national and international collaboration and training

## Slide 61: Acknowledgments
A.Burov, K.Carlson, A.Didenko, N.Eddy, V.Kashikhin, V.Lebedev, J.Leibfritz, M.McGee, S.Nagaitsev, L.Nobrega, H.Piekarz, A.Romanov, G.Romanov, V.Shiltsev, R.Thurman-Keup, A.Valishev, S.Wesseln, D.Wolff (FNAL)
D.Shatilov (BINP)
G. Kafka (IIT)
S. Danilov (ORNL),
S. Antipov (U of Chicago)
J. Cary (Tech-X)
D. Bruhwiler, S. Webb (RadiaSoft)
F.O’Shea, A.Murokh (RadiaBeam)
R.Kishek, K.Ruisard (UMD)
JINR, Dubna

## Slide 62
Backups

## Slide 63: Optical Stochastic Cooling Demonstration
Goal:
  Experimental demonstration of the optical stochastic cooling technique (1st – no optical amplifier, then with OPA)
Why IOTA:
  Need IOTA – low energy (~100 MeV – minimal synchrotron radiation damping) flexible lattice e- storage ring
Motivation:
  Beam cooling for high energy accelerators

## Slide 64: Backstory: Weston Illinois
The footprint of what is now Fermilab started out as a planned community called “Weston”. Developer William Riley promised homes, apartments, shopping centers, parks, etc
After a very small part was built, the project went bankrupt
Riley disappeared (possibly into witness protection).
The local mayors convinced the state to offer up the land to the government to site the proposed N.A.L.
The remains of Weston became “The Village”, which now houses visitors to the lab.

## Slide 65: FAST
Need accelerator R&D beam facilities !

## Slide 66: Space Charge in Linear Optics
System: linear FOFO 100 A linear KV w/mismatch
Result: quickly drives test-particles into the halo
Tech-X, RadiaSoft simulation
DQsc ~ –0.7

## Slide 67: ASTA/IOTA: Original Proposal
This facility began life as the “Advanced Superconducting Test Accelerator (ASTA)”, designed as a test bed for ILC technology
  Front end + 3 cryomodules = ~800 MeV electron
  Designed an electron-based experimental program around this facility
Tacked on the “Integrable Optics Test Accelerator (IOTA)” to test non-linear integrable optics.

## Slide 68: Existing Infrastructure
IOTA capitalizes on the investments made by OHEP for highly successful ILC/SRF R&D Program.
Construction of ASTA (formerly NML) began in 2006 as part of the ILC/SRF R&D Program and later American Recovery and Reinvestment Act (ARRA). The facility was motivated by the goal of building, testing and operating a complete ILC RF unit.
Multi-million (>$90M) investment resulted in the successful commissioning of 1.3 GHz SRF cryomodule (CM2).
  Beam through low-energy photo injector
  Facility nears completion
The addition of IOTA expands scope to host high-intensity accelerator research.

## Slide 69: Possible Implementations
1. The impact of electrons is equal to the total impact of space-charge over the ring
2. The transverse profile of the electron is made the same as that of the proton beam
 use of solenoid
3. The system of magnetized electrons and protons is now dynamically stable
E-lens concept
E-column concept

## Slide 70: IOTA Electron Lens
Capitalize on the Tevatron experience and recent LARP work
Re-use Tevatron EL components

## Slide 71: Quasi-Integrable System
Build V with Octupoles
Only one integral of motion – H
Tune spread limited to ~12% of Q0

## Slide 72: Quasi-Integrable System with Octupoles
While dynamic aperture is limited, the attainable tune spread is large
Ax
Ay
Qx
Qy

## Slide 73: Special Potential – Second Integral of Motion
Find potentials that result in the Hamiltonian having a second integral of motion quadratic in momentum
  All such potentials are separable in some variables (cartesian, polar, elliptic, parabolic)
  First comprehensive study by Gaston Darboux (1901)
Darboux equation
  General solution in elliptic variables x, h , with f and g arbitrary
  Solution that satisfies the Laplace equation

## Slide 74: Maximum Tune Shift
Multipole expansion of U:
For small-amplitude motion to be
stable*, t<0.5
Theoretical maximum nonlinear tune shift per cell is
  0.5 for mode 1, or 50% per cell
  0.25 for mode 2, or 25% per cell
x
c
-c

## Slide 75: Single Particle Dynamics in Integrable Optics
Integer resonance Qy = m
Qx
Qy
Ax
Ay

## Slide 76: Novel Ways to Mitigate Space Charge
Non-linear integrable optics
  All synchrotrons ever built are based on linear optics (magnetic quadrupoles). Non-linearities are handled perturbatively, and eventually lead to instabilities.
  Is has been shown* that non-linear magnetic fields that satisfy a very particular set of conditions can result in stable orbits, but without a unique tune
    Extremely insensitive to harmonic instabilities
    Stable up to space charge tune shifts of order unity!
Electron lens
  A beam of electrons can be used to cancel the space charge effects of the protons
  Demonstrated in the Tevatron
  Used operationally at RHIC
*Danilov, Nagaitsev, PRSTAB 2010