## Slide 1: Particle Accelerators
Eric Prebys, FNAL
Summer Lecture Series

## Slide 2: Comments
This talk will focus primarily on the evolution of the highest energy particle accelerators
  This has largely driven the development of the technology; however
  High energy research machines are a tiny fraction (~1%) of the particle accelerators in use today.
I’ll be fairly technical
  In the end, you should have a fairly quantitative understanding of most of the accelerator jargon you’ll hear in a typical high energy physics talk:
    “Lattice”
    “Beta function”
    “Tune”
    “Emittance”
    “RF”
    etc…

## Slide 3: Relativity and Units
Basic Relativity
Units
  For the most part, we will use SI units, except
    Energy: eV (keV, MeV, etc) [1 eV = 1.6x10-19 J]
    Mass: eV/c2 [proton = 1.67x10-27 kg = 938 MeV/c2]
    Momentum: eV/c [proton @ β=.9 = 1.94 GeV/c]
  In the US and Europe, we normally talk about the kinetic energy (K) of a particle beam, although we’ll see that momentum really makes more sense.
Some Handy Relationships
These units make these relationships really easy to calculate
Remember forever!

## Slide 4: State of the Art: Large Hadron Collider (LHC)
Built at CERN, straddling the French/Swiss border
27 km in circumference
Currently colliding beams of 6.5 TeV/beam
  Design energy of 7 TeV
That’s where we are. Now let’s see how we got here…

## Slide 5: Rewind: Some Pre-History
The first artificial acceleration of particles was done using “Crookes tubes”, in the latter half of the 19th century
  These were used to produce the first X-rays (1875)
  At the time no one understood what was going on
The first “particle physics experiment” told Ernest Rutherford the structure of the atom (1911)
In this case, the “accelerator” was a naturally decaying 235U nucleus
Study the way radioactive particles “scatter” off of atoms

## Slide 6: Man-made Particle Acceleration
The simplest accelerators accelerate charged particles through a static electric field. Example: vacuum tubes (or CRT TV’s)
Cathode
Anode
Limited by magnitude of electric field:
  - CRT display ~keV - X-ray tube ~10’s of keV - Van de Graaf ~MeVs
Solutions:
  Alternate fields to keep particles in accelerating fields -> Radio Frequency (RF) acceleration
  Bend particles so they see the same accelerating field over and over -> cyclotrons, synchrotrons
Old FNAL Cockroft-Walton = 750 kV

## Slide 7: Interlude: Electrons vs. Protons
Electrons are point-like
  Well-defined initial state
  Full energy available to interaction
Protons are made of quarks and gluons
  Interaction take place between these constituents.
  Only a small fraction of energy available, not well-defined.
  Rest of particle fragments -> big mess!
So why not stick to electrons?

## Slide 8: Synchrotron Radiation
As the trajectory of a charged particle is deflected, it emits “synchrotron radiation”
An electron will radiate about 1013 times more power than a proton of the same energy!!!!
Protons: Synchrotron radiation does not affect kinematics very much
  Energy limited by strength of magnetic fields and size of ring
Electrons: Synchrotron radiation dominates kinematics
  To to go higher energy, we have to lower the magnetic field and go to huge rings
  Eventually, we lose the benefit of a circular accelerator, because we lose all the energy each time around.
Radius of curvature
Since the beginning, the “energy frontier” has belonged to proton (and/or antiproton) machines, while electrons are used for precision studies and other purposes.
Now, back to the program…

## Slide 9: The Cyclotron (1930’s)
A charged particle in a uniform magnetic field will follow a circular path of radius
side view
top view
“Cyclotron Frequency”
For a proton: i.e. “RF” range
Accelerating “DEES”: by applying a voltage which oscillates at fc, we can accelerator the particle a little bit each time around, allowing us to get to high energies with a relatively small voltage.
would not work for electrons!

## Slide 10: Round and Round We Go: the First Cyclotrons
~1930 (Berkeley)
  Lawrence and Livingston
  K=80 keV
  Fit in your hand
1935 - 60” Cyclotron
  Lawrence, et al. (LBL)
  ~19 MeV (D2)
  Prototype for many

## Slide 11: Understanding Beam Motion: Beam “rigidity”
The relativistically correct form of Newton’s Laws for a particle in an electromagnetic field is:
A particle of unit charge in a uniform magnetic field will move in a circle of radius
side view
top view
constant for fixed energy!
T-m2/s=V
units of eV in our usual convention
Beam “rigidity” = constant at a given momentum (even when B=0!)
Remember forever!
If all magnetic fields are scaled with the momentum as particles accelerate, the trajectories remain the same
“synchrotron” [E. McMillan, 1945]

## Slide 12: Example Beam Parameters
Compare Fermilab LINAC (K=400 MeV) to LHC (K=7000 GeV)
Parameter | Symbol | Equation | Injection | Extraction
proton mass | m [GeV/c2] |  | 0.938 | 
kinetic energy | K [GeV] |  | .4 | 7000
total energy | E [GeV] |  | 1.3382 | 7000.938
momentum | p [GeV/c] |  | 0.95426 | 7000.938
rel. beta | β |  | 0.713 | 0.999999991
rel. gamma | γ |  | 1.426 | 7461.5
beta-gamma | βγ |  | 1.017 | 7461.5
rigidity | (Bρ) [T-m] |  | 3.18 | 23353.
This would be the radius of curvature in a 1 T magnetic field or the field in Tesla needed to give a 1 m radius of curvature.

## Slide 13: Weak Focusing
Cyclotrons relied on the fact that magnetic fields between two pole faces are never perfectly uniform.
This prevents the particles from spiraling out of the pole gap.
In early synchrotrons, radial field profiles were optimized to take advantage of this effect, but in any weak focused beams, the beam size grows with energy.
The highest energy weak focusing accelerator was the Berkeley Bevatron, which had a kinetic energy of 6.2 GeV
  High enough to make antiprotons (and win a Nobel Prize)
  It had an aperture 12”x48”!

## Slide 14: Strong Focusing
Strong focusing utilizes alternating magnetic gradients to precisely control the focusing of a beam of particles
  The principle was first developed in 1949 by Nicholas Christofilos, a Greek-American engineer, who was working for an elevator company in Athens at the time.
  Rather than publish the idea, he applied for a patent, and it went largely ignored.
  The idea was independently invented in 1952 by Courant, Livingston and Snyder, who later acknowledged the priority of Christophilos’ work.
  Courant and Snyder wrote a follow-up paper in 1958, which contains the vast majority of the accelerator physics concepts and formalism in use to this day!
Although the technique was originally formulated in terms of magnetic gradients, it’s much easier to understand in terms of the separate functions of dipole and quadrupole magnets.

## Slide 15: Combined Function vs. Separated Function
Strong focusing was originally implemented by building magnets with non-parallel pole faces to introduce a linear magnetic gradient
CERN PS (1959, 29 GeV)
=
+
dipole
quadrupole
Later synchrotrons were built with physically separate dipole and quadrupole magnets. The first “separated function” synchrotron was the Fermilab Main Ring (1972, 400 GeV)
=
+
dipole
quadrupole
Fermilab
Strong focusing is also much easier to teach using separated functions, so we will…

## Slide 16: Thin Lens Approximation and Magnetic “kick”
If the path length through a transverse magnetic field is short compared to the bend radius of the particle, then we can think of the particle receiving a transverse “kick”, which is proportional to the integrated field
and it will be bent through small angle
In this “thin lens approximation”, a dipole is the equivalent of a prism in classical optics.

## Slide 17: Quadrupole Magnets* as Lenses
A positive particle coming out of the page off center in the horizontal plane will experience a restoring kick proportional to the displacement
*or quadrupole term in a gradient magnet
just like a “thin lens” with focal length

## Slide 18: What About the Other Plane?
pairs give net focusing in both planes -> “FODO cell”
Defocusing!
Luckily, if we place equal and opposite pairs of lenses, there will be a net focusing regardless of the order.

## Slide 19: Formalism: Coordinates and Conventions
We generally work in a right-handed coordinate system with x horizontal, y vertical, and s along the nominal trajectory (x=y=0).
Particle trajectory defined at any point in s by location in x,x’ or y,y’ “phase space”
unique initial phase space point  unique trajectory
Note: s (rather than t) is the independent variable

## Slide 20: Transfer Matrices
Dipoles define the trajectory, so the simplest magnetic “lattice” consists of quadrupoles and the spaces in between them (drifts). We can express each of these as a linear operation in phase space.
By combining these elements, we can represent an arbitrarily complex ring or line as the product of matrices.
Quadrupole:
Drift:

## Slide 21: Example: Transfer Matrix of a FODO cell
At the heart of every beam line or ring is the basic “FODO” cell, consisting of a focusing and a defocusing element, separated by drifts:
Can build this up to describe any beam line or ring
f
-f
L
L
Remember: motion is usually drawn from left to right, but matrices act from right to left!
Sign of f flips in other plane

## Slide 22: Periodic Systems
You might think, “Start with a beam line, then make a ring out of it.”
  Difficult to solve general case, because it depends on the initial conditions
Therefore, we initially solve for stable motion in a periodic system
We can think of a ring made of identical FODO cells as just the same cell, over and over.
Periodic “cell”
Our goal is to decouple the problem into two parts
  The “lattice”: a mathematical description of the machine itself, based only on the magnetic fields, which is identical for each identical cell
  The “emittance”: mathematical description for the ensemble of particles circulating in the machine.
Extend to beam lines by using boundary conditions (“matching”)
FODO Cell

## Slide 23: General Solution: Betatron Motion
We find (after a lot of algebra) that we can describe particle motion in terms of initial conditions and a “beta function” β(s), which is only a function of location along the nominal path, and follows the periodicity of the machine.
In other words, particles undergo “pseudo-harmonic” motion about the nominal trajectory, with a variable wavelength.
Note: β has units of [length], so the amplitude has units of [length]1/2
The “betatron function” β(s) is effectively the local wavenumber and also defines the beam envelope.
Phase advance
Lateral deviation in one plane
s
x

## Slide 24: Conceptual Understanding of β
It’s important to remember that the betatron function represents a bounding envelope to the beam motion, not the beam motion itself
Normalized particle trajectory
Trajectories over multiple turns (or trajectories of multiple particles!)
β(s) is also effectively the local wave number which determines the rate of phase advance
Closely spaced strong quads  small β  small aperture, lots of wiggles
Sparsely spaced weak quads  large β  large aperture, few wiggles

## Slide 25: Characterizing Particle Ensembles: Emittance
A particle returning to the same point over many terms traces an ellipse, defined by the “beta function”, β, and two additional lattice parameters, α and γ.
An ensemble of particles can characterized by a bounding ellipse, known as the “emittance”
  Definitions vary: RMS, 95%, 99%, etc
NOT to be confused with relativistic β and γ!
Area = επ
Units of length

## Slide 26: Emittance, Beam Size, and Adiabatic Damping
If we use the Guassian definition emittance, then the beam size is
Emittance is constant at a constant energy, but as particles accelerate, the emittance decreases
This is known as “adiabatic damping”. We therefore define a “normalized emittance”
which is constant with energy. Thus, at a particular energy
Relativistic β and γ (yes, I know it’s confusing)

## Slide 27: Emittance and Beam Distributions
As we go through a lattice the shape in phase space varies, by the bounding emittance remains constant
large spatial distribution
small angular distribution
small spatial distribution
large angular distribution
β = max α = 0
maximum
β = decreasing α >0
focusing
β = min α = 0
minimum
β = increasing α < 0
defocusing

## Slide 28: Betatron Tune
As particles go around a ring, they will undergo a number of betatrons oscillations ν (sometimes Q) given by
This is referred to as the “tune”
We can generally think of the tune in two parts:
Ideal orbit
Particle trajectory
6.7
Integer : magnet/aperture optimization
Fraction: Beam Stability

## Slide 29: Tune, Stability, and the Tune Plane
If the tune is an integer, or low order rational number, then the effect of any imperfection or perturbation will tend be reinforced on subsequent orbits.
When we add the effects of coupling between the planes, we find this is also true for combinations of the tunes from both planes, so in general, we want to avoid
Many instabilities occur when something perturbs the tune of the beam, or part of the beam, until it falls onto a resonance, thus you will often hear effects characterized by the “tune shift” they produce.
  For example: the maximum tune shift sets the absolute luminosity limit in a collider
“small” integers
Avoid lines in the “tune plane”

## Slide 30: Longitudinal Motion
We will generally accelerate particles using structures that generate time-varying electric fields (RF cavities), either in a linear arrangement
or located within a circulating ring
In both cases, we want to phase the RF so a nominal arriving particle will see the same accelerating voltage and therefore get the same boost in energy
cavity 0
cavity 1
cavity N
Nominal Energy

## Slide 31: Examples of Accelerating RF Structures
Fermilab Drift Tube Linac (200MHz): oscillating field uniform along length
ILC prototype elipical cell “p-cavity” (1.3 GHz): field alternates with each cell
37->53MHz Fermilab Booster cavity
Biased ferrite frequency tuner

## Slide 32: Phase Stability
A particle with a slightly different energy will arrive at a slightly different time, and experience a slightly different acceleration
Longitudinal motion about stable phase referred to as “synchrotron motion”.
  Takes many revolutions to complete one longitudinal cycle in a synchrotron, so multiple RF cavities are just seen as a vector sum.
Nominal Energy
Off Energy
“slip factor” = dependence of period on momentum
- negative for linacs
- positive for (relativistic)
cyclotrons
- goes from negative to
positive in synchrotrons (“transition”)
Stable point depends on sign.

## Slide 33: Some Important Early Synchrotrons
Berkeley Bevatron,
1954 (weak focusing)
6.2 GeV protons
Discovered antiproton
CERN Proton Synchrotron (PS)
1959
628 m circumference
28 GeV protons
Still used in LHC injector chain!
Brookhaven Alternating Gradient Synchrotron (AGS)
1960
808 m circumference
33 GeV protons
Discovered charm quark, CP violation, muon neutrino

## Slide 34: Getting the Most Energy: The Case for Colliders
If beam hits a stationary proton, the “center of mass” energy is
On the other hand, for colliding beams (of equal mass and energy) it’s
To get the 14 TeV CM design energy of the LHC with a single beam on a fixed target would require that beam to have an energy of 100,000 TeV!
  Would require a ring 10 times the diameter of the Earth!!
Getting to the highest energies requires colliding beams

## Slide 35: Luminosity
The relationship of the beam to the rate of observed physics processes is given by the “Luminosity”
Rate
Cross-section (“physics”)
“Luminosity”
Standard unit for Luminosity is cm-2s-1 Standard unit of cross section is “barn”=10-24 cm2 Integrated luminosity is usually in barn-1,where
nb-1 = 109 b-1, fb-1=1015 b-1, etc
Incident rate
Target number density
Target thickness
Example: MiniBooNe primary target:
For (thin) fixed target:

## Slide 36: Luminosity of Colliding Beams
For equally intense Gaussian beams
Using we have
Geometrical factor: - crossing angle - hourglass effect
Particles in a bunch
Transverse size (RMS)
Collision frequency
Revolution frequency
Number of bunches
Betatron function at collision point  want a small β*!
Normalized emittance
prop. to energy
Particles in bunch
Record e+e- Luminosity (KEK-B): 2.11x1034 cm-2s-1 Record p-pBar Luminosity (Tevatron): 4.06x1032 cm-2s-1 Record Hadronic Luminosity (LHC): 7.0x1033 cm-2s-1 LHC Design Luminosity: 1.00x1034 cm-2s-1

## Slide 37: First e+e- Collider
ADA (Anello Di Accumulazione) at INFN, Frascati, Italy (1961)
  250 MeV e+ x 250 MeV e-
It’s easier to collide e+e-, because synchrotron radiation naturally “cools” the beam to smaller size.

## Slide 38: First Proton Collider: CERN Intersecting Storage Rings (ISR)
1971
31 GeV + 31 GeV colliding proton beams.
  Highest CM Energy for 10 years
Set a luminosity record that was not broken for 28 years!

## Slide 39: SppS: First Proton-Antiproton Collider
Protons from the SPS were used to produce antiprotons, which were collected
These were injected in the opposite direction (same beam pipe) and accelerated
First collisions in 1981
Discovery of W and Z in 1983
  Nobel Prize for Rubbia and Van der Meer
Energy initially 270+270 GeV
Raised to 315+315 GeV
  Limited by power loss in magnets!
design

## Slide 40: Superconductivity: Enabling Technology
The maximum SppS energy was limited by the maximum power loss that the conventional magnets could support.
  LHC made out of such magnets would be roughly the size of Rhode Island!
Highest energy colliders only possible using superconducting magnets
Must take the bad with the good
  Conventional magnets are Superconducting magnets are simple and naturally dissipate complex and represent a great energy as they operate deal of stored energy which must be handled if something goes wrong
R&D into superconducting technology is absolutely critical in the quest for the highest energies (made Tevatron and LHC possible!)
Machine protection is one of the biggest challenges.

## Slide 41: Tevatron: First Superconducting Synchrotron
1968 – Fermilab Construction Begins
1972 – Beam in Main Ring
  (normal magnets)
Plans soon began for a superconducting collider to share the ring.
  Dubbed “Saver Doubler” (later “Tevatron”)
1985 – First proton-antiproton collisions in Tevatron
  Most powerful accelerator in the world for the next quarter century
1995 – Top quark discovery
2011 – Tevatron shut down after successful LHC startup
Main Ring
Tevatron

## Slide 42: Back the present: Large Hadron Collider
Straddles French/Swiss border near Geneva, Switzerland
Tunnel originally dug for LEP
  Built in 1980’s as an electron positron collider
  Max 100 GeV/beam, but 27 km in circumference!!
/LHC
My House (1990-1992)

## Slide 43: LHC Layout and Numbers
Design:
7 TeV+7 TeV proton beams
  7 times Fermilab Tevatron
  Magnets have two beam pipes, one going in each direction.
Stored beam energy 150 times more than Tevatron
  Each beam has only 5x10-10 grams of protons, but has the energy of a train going 100 mph!!
These beams are focused to a size smaller than a human hair to collide with each other!
27 km in circumference
2 major collision regions: CMS and ATLAS
2 “smaller” regions: ALICE and LHCb

## Slide 44: Partial LHC Timeline
2008
  September 10th: First circulating beam
  September 19th: BAD accident brings beam down for over a year (remember what I said about machine protection!)
2009
  November 20th: Particles circulate again
2010
  March 30th: 3.5 + 3.5 TeV collisions
    Energy limited by flaw which caused accident
2012
  April 5th: Energy increased to 4 + 4 TeV
  July 4th: Announced the discovery of the Higgs
2013
  Feb. 14th: Start 2 year shutdown to address design flaw and allow full energy operation
2015
  Mar. 7: protons injected
  May 20: 6.5+6.5 TeV protons collided
The LHC will (probably) be the flagship of the Energy Frontier for at least the next 20 years!

## Slide 45: Evolution of the Accelerator Energy Frontier
~a factor of 10 every 15 years
proton mass
That trend will not continue

## Slide 46: Fermilab Accelerator Complex Today
As LHC takes over the Energy Frontier, Fermilab focuses on intensity-based physics
/Noνa
/400 MeV
/8 GeV
120 GeV+secondaries
Recycler: Formerly for pBar storage, now for proton pre-stacking
Accumulator/Debuncher: Formerly for pBar accumulation, soon muon and proton manipulation (Delivery Ring)
Neutrinos
~45 years old!
LBNF*
(120 GeV)
*proposed

## Slide 47: Possible Future Accelerators
Circular Hadron Colliders
  “Future Circular Collider”: 100 km 50+50 TeV proton collider, based at CERN
Linear e+e- colliders
  “International Linear Collider” (ILC): Up to 500+500 GeV e+e- collider
    Not energy frontier!
  “Compact Linear Collider” (CLIC): Up to 1.5 TeV+1.5 TeV e+e- collider
Muon collider?
  Muons are point-like, like electrons, but don’t radiate as much (good)
  but they are unstable (bad)
  R&D to find a way to cool them and collide them before they decay
  Up to 5 TeV+5 TeV μ+μ-
Even more exotic?
  Plasma wakefield?
  Dielectric wakefield?
  Huge fields, but also huge technical challenges

## Slide 48: Research Machines: Just the Tip of the Iceberg

## Slide 49: Example: Spallation Neutron Source (Oak Ridge, TN)
A 1 GeV Linac loads 1.5E14 protons into a non-accelerating synchrotron ring.
These are fast extracted onto a Mercury target
This happens at 60 Hz -> 1.4 MW
Neutrons are used for biophysics, materials science, industry, etc…

## Slide 50: Light sources: too many to count
Put circulating electron beam through an “undulator” to create synchrotron radiation (typically X-ray)
Many applications in biophysics, materials science, industry.
New proposed machines will use very short bunches to create coherent light.

## Slide 51: Other uses of accelerators
Radioisotope production
Medical treatment
Electron welding
Food sterilization
Catalyzed polymerization
Even art…
In a “Lichtenberg figure”, a low energy electron linac is used to implant a layer of charge in a sheet of lucite. This charge can remain for weeks until it is discharged by a mechanical disruption.

## Slide 52: Further Reading (in Order of Increasing Depth)
My lectures at the 2014 Hadron Collider Physics Summer School
  More details about Fermilab and the LHC (including “The Incident)
  http://tinyurl.com/prebys-hcpss-2014
Fermilab “Accelerator Concepts” (“Rookie Book”)
  http://tinyurl.com/FNAL-concepts
  Particularly chapters II-IV
Edmund Wilson, “Particle Accelerators”
  Concise reference on a number of major topics
  Available in paperback (important if you are paying)
  Good reference for a non-accelerator physicist
Edwards and Syphers “An Introduction to the Physics of High Energy Accelerators”
  My personal favorite
  Concise. Scope and level just right to get a solid grasp of the topic
  Crazy expensive, for some reason.
Helmut Wiedemann, “Particle Accelerator Physics”
  Probably the most complete and thorough book around (originally two volumes)
  Well written
  Scope and mathematical level very high
US Particle Accelerator (USPAS) Course: http://uspas.fnal.gov/

## Slide 53: Backup Slides

## Slide 54: Motivation
Going to higher energies = going back in time

## Slide 55: Where We Are…
Accelerators allow us to go back 13.8 billion years and recreate conditions that existed a few trillionths of a second after the Big Bang
  the place where our current understanding of physics breaks down.
In addition to high energy, we need high “luminosity” that is, lots of particles interacting, to see rare processes.

## Slide 56: Limits to Luminosity*
Total beam current, limited by machine protection(!), e-cloud and other instabilities
β*, limited by
magnet technology
chromatic effects
“Brightness”, limited by
Space charge blowup at low energy
Max beam-beam tune-shift
Geometric factor, related to crossing angle…
*see, eg, F. Zimmermann, “CERN Upgrade Plans”, EPS-HEP 09, Krakow, for a thorough discussion of luminosity factors.

## Slide 57: What next?
The energy of Hadron colliders is limited by feasible size and magnet technology. Options:
  Get very large (~100 km circumference)
  More powerful magnets (requires new technology)
All accelerator magnets based on this
Future magnets could be based on this

## Slide 58: Future Circular Collider (FCC)
Currently being discussed for ~2030s
80-100 km in circumference
Niobium-3-Tin (Nb3Sn) magnets.
~100 TeV center of mass energy

## Slide 59: Other Paths to the Energy Frontier
Leptons vs. Hadrons revisited
  Because 100% of the beam energy is available to the reaction, a lepton collider is competitive with a hadron collider of ~5-10 times the beam energy (depending on the physics).
  A lepton collider of >1 TeV/beam could compete with the discovery potential of the LHC
    A lower energy lepton collider could be very useful for precision tests, but I’m talking about direct energy frontier discoveries.
  Unfortunately, building such a collider is VERY, VERY hard
    Eventually, circular e+e- colliders will radiate away all of their energy each turn
      LEP reached 100 GeV/beam with a 27 km circuference synchrotron!
     Next e+e- collider will be linear

## Slide 60: International Linear Collider (ILC)
LEP was the limit of circular e+e- colliders
  Next step must be linear collider
  Proposed ILC 30 km long, 250 x 250 GeV e+e- (NOT energy frontier)
We don’t yet know whether that’s high enough energy to be interesting
  Need to wait for LHC results
  What if we need more?

## Slide 61: “Compact” (ha ha) Linear Collider (CLIC)?
Use low energy, high current electron beams to drive high energy accelerating structures
Up to 1.5 x 1.5 TeV, but VERY, VERY hard

## Slide 62: Muon colliders?
Muons are pointlike, like electrons, but because they’re heavier, synchrotron radiation is much less of a problem.
Unfortunately, muons are unstable, so you have to produce them, cool them, and collide them, before they decay.

## Slide 63: Wakefield accelerators?
Many advances have been made in exploiting the huge fields that are produced in plasma oscillations.
Potential for accelerating gradients many orders of magnitude beyond RF cavities.
Still a long way to go for a practical accelerator.

## Slide 64: Units of energy: Electron Volts
An “electron-volt” is the energy gained by a particle of unit charge is accelerated over 1V potential
It is really small
  1eV =1.6x10-19 (=.00000000000000000016) Joules - our usual unit of energy.
  A 1 kg weight dropped 1m would have 6x1018 eV of energy!
On the other hand, it’s a very useful unit when talking about individual particles
  If we accelerate a proton using an electrical potential, we know exactly what the energy is.
  It’s also useful when thinking about mass/energy equivalence

## Slide 65: Another way to look at energy…
Quantum mechanics tells us all particles have a wavelength
So going to higher energy allows us to probe smaller and smaller scales
If we put the high equivalent mass and the small scales together, we have…
“Planck Constant”
momentum
as v approaches c

## Slide 66: Understanding Energy
High Energy Physics is based on Einstein’s equivalence of Mass and Energy
All reactions involve some mass changing either to or from energy
If we could convert a kilogram of mass entirely to energy, it would supply all the electricity in the United States for almost a day.
Chemical Explosion
Hydrogen Bomb
.00000005% of mass converted to energy.
~.1% (of just the Hydrogen!) converted.

## Slide 67: Kinetic Energy
A body in motion will have a total energy given by
The difference between this and mc2 is called the “kinetic energy”
Here are some examples of kinetic energy
Rest Energy
Kinetic Energy
For v<<c (speed of light),
Kinetic energy ~ ½mv2
Example | Velocity | Velocity/ Speed of light | Kinetic Energy/(mc2)
Race car | 150 mph | .0000002 | .000000000000025
Apollo 12 (fastest men) | 24,791 mph | .000037 | .00000000068
Proton in the LHC (full energy) | Light minus 2.7 m/s | .999999991 | 7500
Electron in LEP | Light minus 3.6 mm/s | .999999999988 | 203,000

## Slide 68: Equations of Motion
If we go through the equations, keeping only terms which are linear in x and y, we get
Most generic treatment of small deviation from equilibrium in periodic system
  “Hill’s Equation”, first used to study the stability of the lunar orbit
Looks “kinda sorta” like a harmonic oscillator. If K is constant, then not surprisingly, this works!
Local curvature due to dipole field (function of s)
“Rigidity”
Independent of energy for synchrotron!
so try
Periodic

## Slide 69: When is a superconductor not a superconductor?
Superconductor can change phase back to normal conductor by crossing the “critical surface”
When this happens, the conductor heats quickly, causing the surrounding conductor to go normal and dumping lots of heat into the liquid Helium“quench”
  all of the energy stored in the magnet must be dissipated in some way
Dealing with quenches is the single biggest issue for any superconducting synchrotron!
Tc
Can push the B field (current) too high
Can increase the temp, through heat leaks, deposited energy or mechanical deformation

## Slide 70: Quench Example: MRI Magnet*
*pulled off the web. We recover our Helium.

## Slide 71: Partial LHC Timeline
1994:
  The CERN Council formally approves the LHC
2000:
  LEP completes its final run
  First dipole magnet delivered
2007
  Last magnet delivered
  First sector cold
  All interconnections completed
2008
  Accelerator complete
  Last public access
  Ring cold and under vacuum
  September 10th: First circulating beam
  September 19th: BAD accident brings beam down for almost 2 years

## Slide 72: It begins…
9:35 – First beam injected
9:58 – beam past CMS to point 6 dump
10:15 – beam to point 1 (ATLAS)
10:26 – First turn!
…and there was much rejoicing
Commissioning proceeded smoothly and rapidly until September 19th, when something very bad happened

## Slide 73: It Ends: “The Incident”
A quench developed into an arc
This caused Helium to boil
The resulting pressure did a great deal of damage, and kept the machine off for more than a year.
Secondary arcs
Debris in beam vacuum pipe
Clean
Insulation
Soot

## Slide 74: After the Incident
The LHC was off for almost two years to repair the damage and partially address the cause.
2010: Came up at a reduced energy: 3.5 TeV + 3.5 TeV
2012: Increased energy to 4 TeV + 4 TeV
Announced the discovery of Higgs particle July 4, 2012
  Responsible to giving particles mass
  Last piece of the “Standard Model”
2013 Nobel prize to Higgs and Englert

## Slide 75: Plans for LHC
The LHC will be the centerpiece of the world’s energy frontier physics program for at least the next 15-20fd years.
The machine is currently of to fix the issue which cause “the incident”
Accelerator will come back up in 2015 at something close to the design energy
  At least 6.5 TeV/beam
Planning major upgrades to increase luminosity in ~2023

## Slide 76: Some other important accelerators (past):
LEP (at CERN):
  27 km in circumference - e+e- - Primarily at 2E=MZ (90 GeV) - Pushed to ECM=200GeV - L = 2E31 - Highest energy circular e+e- collider that will ever be built. - Tunnel now houses LHC
SLC (at SLAC):
  2 km long LINAC accelerated electrons AND positrons on opposite phases. - 2E=MZ (90 GeV) - polarized - L = 3E30 - Proof of principle for linear collider

## Slide 77: B-Factories
- B-Factories collide e+e- at ECM = M(ϒ(4S)). -Asymmetric beam energy (moving center of mass) allows for time-dependent measurement of B-decays to study CP violation.
KEKB (Belle Experiment):
- Located at KEK (Japan) - 8GeV e- x 3.5 GeV e+ - Peak luminosity >1e34
PEP-II (BaBar Experiment)
- Located at SLAC (USA) - 9GeV e- x 3.1 GeV e+ - Peak luminosity >1e34

## Slide 78: Relativistic Heavy Ion Collider (RHIC)
- Located at Brookhaven:
Can collide protons (at 28.1 GeV) and many types of ions up to Gold (at 11 GeV/amu).
Luminosity: 2E26 for Gold
Goal: heavy ion physics, quark-gluon plasma, ??

## Slide 79: Continuous Electron Beam Accelerator Facility (CEBAF)
Locate at Jefferson Laboratory, Newport News, VA
6GeV e- at 200 uA continuous current
Nuclear physics, precision spectroscopy, etc

## Slide 80: Natural Particle Acceleration
Radioactive sources produce maximum energies of a few million electron volts (MeV)
Cosmic rays reach energies of ~1,000,000,000 x LHC but the rates are too low to be useful as a study tool
  Not enough “luminosity”
However, low energy cosmic rays are extremely useful for detector testing, commissioning, etc.
Max LHC energy

## Slide 81: Onward and Upward!
Cyclotrons were limited by three problems
  Constant frequency breaks down at ~10% speed of light
    Solved with variable frequency “synchro-cyclotrons”  phase stability (more about this later)
  As energy goes up, magnet gets huge
  Beams are not well focused and get larger with energy
Two major advances allowed accelerators to go beyond the energies and intensities possible at cyclotrons
  “Synchrotron” – in which the magnetic field is increased as the energy increases (proportional to momentum), such that particles continue to follow the same path .
  “Strong focusing” – a technique in which magnetic gradients (non-uniform fields) are used to focus particles and keep them in a smaller beam pipe than was possible with cyclotrons.
Note: still plenty of uses for cyclotrons (simple, inexpensive, rapid cycling)
  Medical treatments
  Isotope production
  Nuclear physics