## Slide 1: Fermilab Accelerator Complex
Eric Prebys
Fermilab AD/APC

## Slide 2: Fermilab: Early History
1963 – Committee chaired by Norman Ramsey recommends the construction of a 200 BeV synchrontron
  to be located at Berkeley (of course)
1965 - Joint Committee on Atomic Energy (JCAE) and the National Academy of Sciences (NAS) endorse the Ramsey Report
  but as a “National Accelerator Lab”, with a nation-wide site selection.
1966 – Weston, IL chosen as the site
1967 – Cornell physicist Robert Wilson named first director
1968 – Construction of NAL begins
1972 – First 200 GeV beam in the Main Ring (400 GeV later that year)
  Extracted to three fixed target, experimental beam lines: Meson, Neutrino, and Proton
1974 – Iconic “High Rise” completed. Lab dedicated to Enrico Fermi, and renamed “Fermi National Accelerator Laboratory”
  Fermi’s widow, Laura, attended the ceremony

## Slide 3: What Was Weston?
Note round thing in middle
In 1964, developer William Riley began construction of Weston, IL, a planned community with houses, apartments, parks, churches, and shopping centers.
The development went bankrupt less than a year later, after the completion of only a small portion.
Local politicians convinced the state to propose the site for to the AEC for the new National Accelerator Lab
  Residents did not realize they would have to move!
In 1996, Weston site was chosen out of 126 proposals with over 200 sites.
The small completed part became the Fermilab Village.
Since it was the 60s, the mob had of course been involved. Faced with bankruptcy and threats, Riley testified against them and subsequently disappeared into witness protection.

## Slide 4: Main Ring: First Separated Function Synchrotron
Strong focusing was originally implemented by building magnets with non-parallel pole faces to introduce a linear magnetic gradient
CERN PS (1959, 29 GeV)
=
+
dipole
quadrupole
Later synchrotrons were built with physically separate dipole and quadrupole magnets. The first “separated function” synchrotron was the Fermilab Main Ring (1972, 400 GeV)
=
+
dipole
quadrupole
Fermilab

## Slide 5: Tevatron: First Superconducting Synchrotron
From the beginning, Wilson was making plans for a superconducting ring to share the tunnel with the Main Ring
  Dubbed “Saver Doubler” (later “Tevatron”)
1982 – Magnet installation complete
1985 – First proton-antiproton collisions observed at CDF (1.6 TeV CoM). Most powerful accelerator in the world for the next quarter century
  Alternated collider and fixed target program.
1995 – Top quark discovery
Late 1990’s – major upgrades to increase luminosity, including separate ring (Main Injector) to replace Main Ring
  Also removed extraction hardware to eliminate Tevatron fixed target program.
1999 – Tevatron Energy reaches 1.96TeV CoM energy
2011 – Tevatron shut down after successful LHC startup
Main Ring
Tevatron

## Slide 6: Fermilab Firsts and Records
Firsts:
  First separated function synchrotron:
    Main Ring, 1972
  First superconducting synchrotron/collider
    Tevatron, 1983 (first collisions in 1986)
  First permanent magnet storage ring
    Recycler, 2000
Records:
  Highest energy proton beam
    Main Ring, 1972 (breaks AGS record)1983 (broken by Tevatron)
    Tevatron, 1983-2008 (broken by LHC)
  Highest energy hadron collider
    Tevatron, 1986 (breaks SppS record)2009 (broken by LHC)
  Highest hadronic luminosity
    Tevatron, 2005 (broke ISR *p-p* record!)  2011 (broken by LHC)
  Highest energy p-pbar collider
    Tevatron, 1986 (breaks SppS record) present
  Highest p-pbar luminosity
    Tevatron, 1992 (broke SppS record) present

## Slide 7: Fermilab Accelerator Complex Today
As LHC takes over the Energy Frontier, Fermilab focuses on intensity-based physics
/Noνa
/400 MeV
/8 GeV
120 GeV+secondaries
Recycler: Formerly for pBar storage, now for proton pre-stacking
Accumulator/Debuncher: Formerly for pBar accumulation, soon muon and proton manipulation (Delivery Ring)
Neutrinos
~45 years old!

## Slide 8: Why Multiple Stages?
At low energies, space charge is trying to blow up beams, so you want to accelerate them as quickly as possible to energies where relativistic effects prevent this
  start with a linear accelerator
The energy range of a single synchrotron is limited by
  Beams get smaller as as they accelerate ( ), so an aperture large enough for the injected beam is unreasonably large at high field.
  Hysteresis effects result in excessive nonlinear terms at low energy
Typical range 10-20 for colliders, larger for fixed target
  Fermilab Main Ring: 8-400 GeV (50x)
  Fermilab Tevatron: 150-980 GeV (6.5x)
  LHC: 400-7000 GeV (17x)
Higher energy beams require multiple stages of acceleration, with high reliability at each stage
How is this done?

## Slide 9: Getting started: Ion sources
CERN proton source
CERN Lead source
Typically 10s of keV and mAs to 10s of mA of current. Want to accelerate as fast as possible before space charge blows up the beam!
FNAL H- source. Mix Cesium with Hydrogen to add electron. (why? we’ll get to that)

## Slide 10: Initial Acceleration
Old: Static
Static acceleration from Cockcroft-Walton. FNAL = 750 keV
max ~1 MeV
New: RF Quadrupole (RFQ)
RF structure combines an electric focusing quadrupole with a longitudinal accelerating gradient.

## Slide 11: (New) Fermilab Front End
The front end of any modern hadron accelerator looks something like this:
Low Energy Beam Transport (LEBT, pronounced “lebbit”): 35 keV
Medium Energy Beam Transport (MEBT, pronounced “mebbit”): 750 kEV
Redundant H- sources: 0-35 keV
Solenoidal focusing for low energy beam
200 MHz RFQ: 35750 keV
beam

## Slide 12: Linac (750keV400 MeV)
Because the velocity is changing quickly, the first linac is a 200 MHz Drift Tube Linac (DTL, aka “Avarez Linac”), which can be beta-matched to the accelerating beam.
Put conducting tubes in a larger pillbox, such that inside the tubes E=0
Bunch of pillboxes
Gap spacing changes as velocity increases
Drift tubes contain quadrupoles to keep beam focused

As energy gets higher, switch to 800 MHz “p-cavities”, which are more efficient (added in 1990s)

## Slide 13: Linac -> synchrotron injection
Eventually, the linear accelerator must inject into a synchrotron
In order to maximize the intensity in the synchrotron, we can
  Increase the linac current as high as possible and inject over one revolution
    There are limits to linac current
  Inject over multiple (N) revolutions of the synchrotron
    Preferred method
Unfortunately, Liouville’s Theorem says we can’t inject one beam on top of another
  Electrons can be injected off orbit and will “cool” down to the equilibrium orbit via synchrotron radiation.
  Protons can be injected a small, changing angle to “paint” phase space, resulting in increased emittance
Linac emittance
Synchrotron emittance

## Slide 14: Ion (or charge exchange) injection
Instead of ionizing Hydrogen, and electron is added to create H-, which is accelerated in the linac
A pulsed chicane moves the circulating beam out during injection
An injected H- beam is bent in the opposite direction so it lies on top of the circulating beam
The combined beam passes through a foil, which strips the two electrons, leaving a single, more intense proton beam.
Fermilab was converted from proton to H- during the 70’s (present chicane uses three magnets)
CERN still uses proton injection, but is in the process of upgrading (LINAC4 upgrade)
Unfortunately, this can only be done once!
Circulating Beam
Beam at injection
H- beam from LINAC
Stripping foil
Magnetic chicane pulsed to move beam out during injection

## Slide 15: Booster
Accelerates the 400 MeV beam from the Linac to 8 GeV
    Operates in a 15 Hz offset resonant circuit
      Cannot alter beam structure
      That’s why Mu2e needs other rings
    Sets fundamental clock of accelerator complex!
More or less original equipment
  45+ years old
Supplying beam to neutrino program and Mu2e will require ~doubling output
  Hardware limits  Improve RF system
  Radiation limits  Improve acceleration efficiency to reduce losses.
 “Proton Improvement Plan” (whole separate talk)

## Slide 16: Injection and extraction from synchrotrons
After the initial ion injection, protons must be transferred all at once.
We would ideally like to extract (or inject) beam by switching a magnetic field on between two bunches (order ~10-100 ns)
Unfortunately, getting the required field in such a short time would result in prohibitively high inductive voltages, so we usually do it in two steps:
fast, weak “kicker”
slower (or DC) extraction magnet with zero field on beam path.
Injection is just extraction in reverse

## Slide 17: Extraction hardware
“Lambertson”: usually DC
B
B
circulating beam (B=0)
circulating beam (B=0)
current “blade”
return path
Septum: pulsed, but slower than the kicker
“Slow” extraction elements
“Fast” kicker
usually an impedance matched strip line, with or without ferrites
At Fermilab, the Booster septum transfers to the Main Injector Lambertson

## Slide 18: Main Injector/Recycler
Main Injector
  Accelerates protons (or pBars) from 8 GeV to 120 or 150 GeV
  Can hold up to 12 Booster batches
Recycler
  Permanent magnet 8 GeV storage ring
  During Tevatron program, used to store pBars
    All particles had to pass through Main Injector first!
  Currently being configured to pre-stack protons for loading into the Main Injector
  In the future, it will be used to re-bunch protons for the g-2 and Mu2e experiments.

## Slide 19: A Tight Fit

## Slide 20: Box Car Stacking/ Slip Stacking
The Recycler and Main Injector are 7 times the circumference of the Booster
  There are 7 “slots” to inject Booster batches
One bunch is injected into one of the 7 slots
This process can continue until up to 6/7 slots are filled (“boxcar stacking”).
At this point, we can accelerate and extract the beam, or…
Decelerate these bunches slightly
Inject a new batch is injected into the empty slot.
Because it it a slightly different velocity it will “slip” relative to the other bunches.
Continue until there are 6 double bunches, which can then be accelerated and extracted.
Note: two is the limit because of momentum aperture.
`
Slip stacking was done in the Main Injector to increase protons to pBar and NuMI
Being commissioned in Recycler

## Slide 21: Fermilab Antiproton Source: OBSOLETE
120 GeV protons strike a target, producing many things, including antiprotons.
a Lithium lens focuses these particles (a bit)
a bend magnet selects the negative particles around 8 GeV. Everything but antiprotons decays away.
pBars were “stacked” in the two part Accumulator/Debuncher rings
  Later “stashed” in Recycler
Took ~1 day to make enough Pbars for one Tevatron “store”, which lasted a day
  “Stack and Store” cycle
The Accumulator ring will be dismantled for parts, and the Debuncher Ring (”Delivery Ring”) will be re-tasked for g-2 and Mu2e.

## Slide 22: NOnA Time Line Improvements
300 kW
700 kW
Tevatron era: must allow time at injection energy to load protons into Main Injector
Upgrade: a new transfer line will allow us to “prestack” in the Recycler
Up to ~5x1020 protons/year that cannot be used by NOnA

## Slide 23: Resonant Extraction
Some experiments don’t want all the beam at once.
Use nonlinear magnets to drive a harmonic instability
  quadrupoleshalf-integer: Main Ring, Tevatron, Main Injector (120 GeV Program)
  sextupolesthird-integer: Delivery Ring for Mu2e
Extract unstable beam as it propagates outward
  Standard technique in accelerator physics
Use electrostatic septum followed by Lambertson
Extraction Field
Wire or foil plane
Unstable beam motion in N(order) turns
Lost beam
Extracted beam
Lambertson

## Slide 24: g-2 and Mu2e Proton Delivery
Booster
Main Injector/Recycler
Delivery Ring (formerly pBar Debuncher)
Mu2e
Common to both:
  One Booster “batch” is injected into the Recycler (8 GeV storage ring).
    4x1012 protons
    1.7 msec long
  It is divided into 4 bunches of 1012 each
g-2:
  Bunches are extracted to a muon production target (former pBar target location)
  Muons circulate in Delivery Ring until all pions decay away
  Muons are extracted to g-2 precession ring (transported from Brookhaven)
Mu2e:
  Bunches are extracted directly to the Delivery Ring
    Period = 1.7 msec
  As each bunch circulates, it is resonantly extracted to produce the desired beam structure.
    Bunches of ~3x107 protons each
    Separated by 1.7 msec

## Slide 25: 120 GeV Program
120 GeV beam from the Main Injector passes through a stub of the original Main Ring in the Tevatron Tunnel
Primary and secondary beams. Support for test beams and HEP experiments: MIPP, SeaQuest, etc.

## Slide 26: Beam Delivery to SeaQuest
Once a minute, 6 booster batches are loaded into the Main Injector
These resonantly extracted over 5 seconds through the Main Ring stub, through the Switchyard to SeaQuest
Time substructure
~81 53 MHz bunches

## Slide 27: Controlling the Complex
The Booster resonant circuit sets a fundamental clock for the complex: 15 Hz
Protons can be arbitrarily routed and handled at the level of one Booster “batch”
  Size controlled by length of linac injection
    1-15 “turns” ≈ 0.3-4.5x1012 protons
    1.6 msec train of 53 MHz bunches.
  Smaller or shorter extractions can be made by phasing the extraction and dump kickers to extract a partial batch
    Very wasteful: historically used for loading Tevatron protons
Each machine handles protons based on a two digit hexadecimal “Event Reset”, produced by the Time Line Generator
  Generally Linac: $01-$0F, Booster: $10-$1F, Main Injector: $20-$2F, Switchyard: $30-$3F, etc
Examples
  Linac studies: $0A
  MiniBooNE: $0F$1D
  NuMI: $0F$17$23
  Can have multiple clock types in a cycle to control different parts of, eg, Main Injector Ramp

## Slide 28: Proton Demands
Slow extraction experiments take a tiny fraction of the protons, but take a significant fraction of the timeline from other experiments
  SeaQuest uses about .4% of the protons NuMI does, but results in a 3.3% reduction in the protons to NuMI.
~80kW @ 8 GeV