## Slide 1: Muon Needs of Project X
Eric Prebys/Keith Gollwitzer

## Slide 2: Muon Task Force
Experiments:
  Yoshitaka Kuno, Osaka University, Japan
  Jim Miller, Boston University
Accelerator:
  Eric Prebys, FNAL
  Keith Gollwitzer, FNAL

## Slide 3: Potential Muon Experiments* at Project X
Muon Charged Lepton Flavor Violation
  meg
  meee
  m+Ne+N (muon to electron conversion)
Muon electric dipole moment (EDM)
Muon lifetime
Muonium (m+e-)  anti-muonium (m-e+)
*neutrino factory and muon collider are explicitly excluded from this list.
chosen as “flagship” experiment

## Slide 4: Muon-to-Electron Conversion: m+N  e+N
Similar to megwith important advantages:
  No combinatorial background
  Because the virtual particle can be a photon or heavy neutral boson, this reaction is sensitive to a broader range of BSM physics
Relative rate of meg and mNeN is the most important clue regarding the details of the physics
m
105 MeV e-
When captured by a nucleus, a muon will have an enhanced probability of exchanging a virtual particle with the nucleus.
This reaction recoils against the entire nucleus, producing the striking signature of a mono-energetic electron carrying most of the muon rest energy

## Slide 5: Pre-Project X Mu2e Experiment and Limitation
Will use existing accelerator complex.
μ- are accompanied by e-, π-, …
Extinction required to make prompt background ~equal to all other backgrounds
  1 out of time proton per 109 in time protons.
Expect a single event sensitivity of 2x10-17 (4 order of magnitude improvement)
Limited by
  p- content in beam
  Time distribution of muons “straggling” down the transport line
  Energy smearing due to required thick target.

## Slide 6: Caveat
Mu2e is proposed to run using modifications to the existing Fermilab complex
Sensitivity goal: < 1x10-16 (a four order of magnitude improvement over existing limits)
This is a challenging goal, and achieving it is by no means assured.
The beam available at Project X could potentially extend this significantly
  We assume a working goal of <1x10-18
There are big challenges to doing this that have not been addressed at any credible level.
Proposals have not advanced beyond the cartoon stage at this point.
Side note: you might build a very different experiment if Mu2e sees something!

## Slide 7: Next to Next Generation Experiment
To hope to go beyond the limit of Mu2e, one needs the following:
  Improved pion suppression
    Longer time/beam line for pions to decay away.
  Narrower momentum spread
    Muons can be stopped in a narrower target, so there is less problem with multiple scattering before the detector
  Narrower time distribution for arriving muons
    Allows one to set the live window closer to the proton arrival
    Particularly important for different target nuclei
      If a signal is see, exploring different nuclear key to understanding fundamental nature
      Heavier nuclei have shorter lifetimes, eg t(m+Au) = 72 ns
  Better suppression between pulses
    10-1010-12
Two very different proposals have been put forth to achieve these goals.

## Slide 8: FFAG-based Proposal
Similar to PRISM/PRIME, proposed at J-Parc
Produced muons are captured in an FFAG storage ring and phase rotated, while remaining pions decays away

## Slide 9: Ionization Cooling Channel Propoposal
Based on R&D for muons collider/neutrino factories
By cooling and decelerating, we can take advantage of higher momentum pions, for which the yield is much higher.
target
325 MHz* capture/p decay
162.5 MHz bunch rotation
Transverse cooling
6D cooling
deceleration
*optimum frequencies for capture and phase rotation still under study

## Slide 10: Primary Beam Requirements
Unfortunately, the primary beam requirements are very different in the two cases
  FFAG case
    Limited by the maximum injection/extraction kicker in the FFAG
      Assume 1 kHz
    1MW @ 1kHz = 2x1012 protons/pulse
    10 ns pulse length
    CANNOT come directly from linac
    Need:
333 ms@ 1 mA
100 ns gap for extraction kicker
Stripper/Accumulator
Phase Rotator
to production
target

## Slide 11: Beam Requirements (cont’d)
  Ionization Channel Cooling Case
    In this case, beam could come directly from Project X linac
      No need for bunching or stripping
    Directly produce beam structure needed by experiment
    E.g.
      1 MW @ 500 kHz
        10 mA (2x108 protons/325 MHz bunch)
        22 bunches=68 ns
        Every 2 msec

## Slide 12: Comparing the Two Techniques
Both proposals have significant synergy with muon collider/neutrino factories
  FFAG proton accumulator/buncher similar to the NF&MC proton driver
  Ionization cooling is obvious
Clearly the ioniziation cooling channel is much simpler from the standpoint of primary protons
Both techniques for muon transport are very complicated and beyond state of the art:
  Need to study in detail to do a proper comparison.